Analysis of temporal and spatial patterns of

NH3 and NH4+ over the UK - 2007

Annual report to DEFRA

RMP 1906

Y.S. Tang, N. van Dijk, M. Anderson, I. Simmons, A.J. Dore, U Dragosits, W.J. Bealey, D Leaver, R. I. Smith & M.A. Sutton

Centre for Ecology and Hydrology (Edinburgh Research Station)

Bush Estate, Penicuik, Midlothian, EH26 0QB, UK.

August 2008

| Client: Defra |
| --- |
| Client Project number: RMP 1906 | CEH Project number: C03124 |
| Project Title: UK National Ammonia Monitoring Network Annual Report: Analysis of spatial and temporal patterns of NH3 and NH4+ over the UK - 2007. |
| Start date: 01/05/06 | Completion date: 31/12/08 |
| Client Project Officer: Soheila Amin-Hanjani / Sarah Honour |
| CEH Project Officer: Dr M.A. Sutton |
| Main authors: Y.S. Tang, N. van Dijk, M. Anderson, I. Simmons, A.J. Dore, U Dragosits, W.J. Bealey, D Leaver, R. I. Smith & M.A. Sutton |
| Report approved for release by: Dr M. A. Sutton |
| Reporting period: Jan 07 – Dec 07 |
| Report date: 21 August 08 |
| Report Number: AS 08/06 |
| Report Status: Annual Report |

This report is a confidential document prepared under contract to the UK Department for Environment, Food and Rural Affairs (Defra). It should not be distributed or quoted without the permission of both the Centre for Ecology and Hydrology (CEH) and Defra.

# Executive Summary

Operation of the NAMN

- The National Ammonia Monitoring Network (NAMN) applies the established DEnuder for Long-Term Atmospheric (DELTA) system, together with the high sensitivity Adapted Low-cost Passive High Absorption (ALPHA) sampler, with the latter subject to continuous calibration.

- A robust long-term baseline on gaseous NH3 (since Sep 1996) and aerosol NH4+ (since Jan 1999) allows changes in atmospheric NHx to be quantified spatially across the UK, which will provide a basis to verify compliance with international agreements.

- The DELTA system used in the NAMN also provides a foundation for monitoring of other atmospheric components at a subset of sites, including monthly measurements of gaseous HNO3, SO2, HCl and aerosol NO3-, SO42-, Cl-, plus base cations Na+, Ca2+ and Mg2+, as part of the Nitric Acid Monitoring Network. Results of those measurements are reported separately under the Acid Deposition Monitoring contract.

Network results: QAQC

- Quality Assurance is maintained through the careful implementation of established sampling protocols, and monitoring of laboratory performance through participation in the EMEP and WMO-GAW inter-comparison schemes for analytical laboratories.

- Data quality is assessed using set Quality Control criteria:  a) capture efficiency using two denuders in the DELTA systems and b) coefficient of variation for ammonia concentrations with the triplicate ALPHA samplers.

Network results: Spatial patterns and seasonal variability

- Data are mounted on the internet at the web page of the UK NAMN which can be found at: http://www.uk-pollutantdeposition.ceh.ac.uk

- Site mean annual concentrations of gaseous NH3 measured in 2007 were in the range 0.04 - 9.3 g m-3. Site mean annual concentrations of aerosol NH4+ measured in 2007 were in the range 0.16-1.5 g m-3 and are spatially more even, as predicted.

- The measurements have been used to construct maps of NH3 and aerosol NH4+ concentrations over the country.  The NAMN is currently based on around 95 sites, and the high spatial variability of NH3 concentrations demonstrates that this large number of sites is necessary. Aerosol NH4+, a secondary product is spatially more even and is monitored at a smaller number of sites (currently 46).

- The measurements show a broad pattern of small air concentration in the NW Scottish Highlands (<0.2 g m-3) and larger concentrations across much of lowland Britain (1-3 g m-3), as well as peaks in intensive agricultural areas (up to 22 g m-3).

- Measurements in remote sites show a strong seasonal cycle with the largest concentrations in summer and smallest in winter.

- In sheep dominated areas there is an extremely strong seasonal cycle with largest concentrations in summer, in some cases up to a factor of 100 larger than winter concentrations. This is expected to relate to the increased potential for grazing emissions in warm summer conditions.

- A more complex seasonal pattern is seen in cattle, pig and poultry dominated areas (e.g. East Anglia). In these situations strong spring and autumn peaks in NH3 concentrations are also recorded, which almost certainly reflect emissions from the land spreading of wastes from housed livestock to spring growth or after harvest.

- Measurement data are used to calibrate the FRAME atmospheric transport model, and the model output is then combined with the CBED deposition model to provide a best estimate of ammonia dry deposition of 53 kt N yr-1 for 2007.

Network results: Trends

- Eleven years of NH3 data (1997-2007) and 9 years of aerosol NH4+ data (1999-2007) were analysed. Trends are not easily detectable at individual sites due to significant inter-annual variability linked to meteorological differences and the effect of local emissions at different times of the year. For this reason, a trend assessment on the results was made from multiple sites.

- A key benefit of the large number of sites in the NH3 network is that group analysis can be conducted according to the major source sectors (AENEID model). Changes in estimated emissions for different sectors (cattle, sheep, urban etc) are not the same over the course of the network and differences may therefore be expected.

- Overall the data show informative trend differences in NH3 concentrations. There are currently no detectable trends in aerosol NH4+ concentrations, indicating that a longer measurement period is needed before trends can be detected.

- In pig-poultry dominated areas, there is a slight (non-significant) reduction in NH3 concentrations.  This is consistent with (but not as large as) the estimated reduction in NH3 emissions from these sectors.

- In cattle dominated areas, there is a slight (non-significant) increase in NH3 concentrations, although there have been no increase in NH3 emissions from these sectors since 2000.

- In background sites (defined by 5 km grid average emissions <1 kg N ha-1 yr-1), there is a tendency for NH3 concentrations to have increased over the monitoring period, even though emissions are not estimated to have increased. This may be a feature of the reduction in SO2 emissions over the period, leading to a longer atmospheric lifetime of NH3, thereby increasing NH3 concentrations in remote areas.

- In sheep dominated areas, there was also a slight (non-significant) increase in NH3 concentrations. However, the analysis was based on results from 5 sites only.

Local variability assessment

- The first year of measurements has been completed from Local scale variability assessment of ammonia, at a UK Southern Scottish study Landscape.  Parallel inventorying activities conducted by the NitroEurope Integrated Project will allow a detailed interpretation of these measurements providing information to improve understanding on sub-grid variability and site representativity.

Related activities

- Throughout the contract period, CEH staff continued to contribute expertise related to ammonia and monitoring to the groups under the UNECE Convention on Long-range Transboundary Air Pollution (CLRTAP), EMEP-TFMM, as well as to the Centre for European Normalization (CEN) Technical Committee 264/Working Group 11 on standardization of diffusion based air monitoring methods.

Contents

Executive Summary	2

1. Introduction	6

2. Network Structure	6

2.1. Integration of the Nitric Acid Monitoring Network with the NAMN	12

3. Sampling Methods	12

3.1. Active sampling method: DELTA system	12

3.1.1. Sampling train	12

3.1.2. Denuder extraction and chemical analysis	13

3.1.3. Calculation of NH3 concentrations	13

3.1.4. Calculation of NH4+ concentrations	14

3.2. Passive Diffusion Samplers	14

3.2.1. Analysis of passive samplers	14

3.2.2. Calculation of NH3 concentrations	15

3.2.3. Calibration of passive samplers	15

3.3. Quality Assurance and Quality Control of sampling methods	15

4. Results and Discussion	16

4.1. Performance of the network	16

4.2. Measurement reproducibility	17

4.3. Intercomparison of delta and passive sampling methods	18

4.4. Summary of measurements	21

5. TEMPORAL PATTERNS	24

5.1. Mean Temporal Patterns of NH3	24

5.2. Mean Temporal Patterns of aerosol NH4+	24

5.3. Comparison by dominant emission sources	24

6. SPATIAL PATTERNS	24

6.1. Local Variability	24

7. Trends in ammonia concentrations	24

7.1. Emission sector: Background	24

7.2. Emission sector: Cattle	24

7.3. Emission sector: Pig & Poultry	24

7.4. Emission sector: Sheep	24

8. trends in aerosol ammonium concentrations	24

8.1. Estimation of UK ammonia dry deposition	24

9. ACKNOWLEGEMENTS	24

10. REFERENCES	24

11. APPENDIX	24

11.1. Monthly ammonia data in the UK NAMN	24

11.2. Monthly particulate ammonium data in the UK NAMN	24

# Introduction

The UK NAMN has been operated by the Centre for Ecology and Hydrology (CEH) on behalf of the Department for Environment, Food and Rural Affairs (Defra) and the Devolved Administrations, and its predecessors since September 1996. The aims of the NAMN are to explore spatial and temporal patterns in ammonia (NH3) concentrations, compare results with dispersion models, and contribute to national Nitrogen (N) deposition estimates. Since 1999, the network has also included measurements of ammonium (NH4+) particles.

In this annual report, we summarize the sampling methods and measurement data from the NAMN for 2007 and compare this against previous years. Initial results from a local variability assessment of ammonia, carried out in conjunction with detailed NitroEurope Landscape Analysis at a UK Southern Scottish study Landscape are also reported here.

# Network Structure

Given the high spatial variability of NH3, the strategy for the network was to sample at a large number of sites to map the UK NH3 concentration field, using low-frequency sampling (monthly) to allow temporal patterns and long-term trends to be assessed at a low cost. To address the issue of site representativity, assessment of sub-grid variability at selected locations have also been made (Tang et al. 2001a, Sutton et al. 2004). There are currently 95 sites in the network (Figure 1A), details of which are provided in Table 1.

Overall, the NAMN structure currently consists of:

| Site Type | Number |
| --- | --- |
| DELTA sites sampling gaseous NH3 | 59 |
| DELTA sites also sampling aerosol NH4+ | 46 |
| DELTA sites also sampling gaseous HNO3, SO2, HCl & aerosol NO3-, SO42, Cl-, Na+, Ca2+, Mg2+)as part of the HNO3 Monitoring Network | 30 |
| ALPHA sites sampling gaseous NH3 only | 50 (this includes the 8 ICP sites) |
| Intercomparison sites with both DELTA & ALPHA | 14 |
| Total number of sites | 95 |

(A)  NAMN 95 sites	                (B) HNO3 Network 30 Sites

Figure 1:  Map of (A) 95 site NAMN for NH3 and NH4+, and (B) 30 site HNO3 network for HNO3, NO3- and related acid gas/particle measurements.

Table 1: List of sites in ammonia monitoring network (Jun 08) (See footnotes at end of Table).

| No | Site Name | Site Operator | Nature Reserve Status | Other air monitoring | Map Ref. | Type | Start | End |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | Bush 1 | CEH Edinburgh |  | HNO3 NW | nt243642 | D,D,F,T | Apr '96 |  |
| 2 | Bush 2 | CEH Edinburgh |  | SO2, O3, NOx | nt247638 | T | Apr '96 |  |
| 3 | Inverpolly | SNH | NNR | HM | nc187088 | D,F,T | Nov ‘95 | Jul ’04 (D), Aug ’06 (T) |
| 3B | Inverpolly | SNH | NNR |  | nc187087 | D,F,T | Jul ’04 (D), Aug ’06 (T) |  |
| 4 | Penallt | Gwent Wildlife Trust | SSSI | HM | so523095 | D | Sep '96 |  |
| 5 | Priddy | Somerset Wildlife Trust | SSSI |  | st525526 | D | Sep '96 | Dec '01 |
| 6 | Holme Lacy | Holme Lacy College |  |  | so554357 | D,F | Mar '97 | Dec ‘05 |
| 6B | Rosemaund | ADAS |  | HNO3 NW, NO2, | so564476 | D,F | Jan ‘06 |  |
| 7 | Glenshee | G. Cruikshanks | NNR |  | no117693 | D | Sep '96 | May '00 |
| 7B | Gulabin Lodge | G. Fischnaller | NNR |  | no110701 | D,F | Apr ‘00 | Dec ‘05 |
| 8 | Stackpole | CCW | NNR / SSSI | SO2 | sr982947 | D | Sep '96 | Dec '97 |
| 8B | Orielton | CCW | NNR / SSSI | SO2 | sr954992 | D,F | Jan '98 | Dec ‘05 |
| 8C | Narberth | Pembrokeshire County Council |  | HNO3 NW, NO2, AURN (PM10, NOx) | Sn146127 | D,F | Jan ‘06 |  |
| 9 | Brown Moss | A. Bushnell | LNR / SSSI |  | sj559396 | D,T | Sep '96 | May '98 |
| 9B | Brown Moss 2 | J. Ashley | LNR / SSSI |  | sj563390 | D,T | May '98 |  |
| 10 | Bure Marshes | English Nature | NNR |  | tg334161 | D | Nov '96 |  |
| 11 | Mere Sands Wood | Lancashire Wildlife Trust | LNR |  | sd447157 | D,F,T | Sep '96 |  |
| 12 | Halladale | Fountain Forestry |  | HNO3 NW, NO2 | nc902488 | D,F | Jan '97 |  |
| 13 | Aston Rowant | English Nature | NNR |  | su727979 | D | Sep '96 |  |
| 14 | Ellon Ythan | MLURI |  |  | nj945304 | D | Sep '96 |  |
| 15 | Llynclys Common | D. Pedlow | SSSI |  | sj273237 | D,T | Sep '96 |  |
| 16 | Northallerton | K. Hardisty |  |  | se360930 | D,F | Jan '97 |  |
| 17 | Easingwold | Hawkhill College |  |  | se540675 | D,F | Jan '97 |  |
| 18 | Auchencorth Moss | CEH Edinburgh |  | SO2, O3, NOx, HM | nt221562 | D,D,F,T | Apr '96 |  |

Note: S3B Inverpolly 2 (met enc.), relocated from original S3 Inverpolly site located at Knockan cottage. S3B is ~100m away within a meteorological enclosure. Parallel measurements were made for 2 years to check that concentrations were not different at new site, before the Knockan site was closed down.

Table 1: List of sites in ammonia monitoring network (Jun08) cont.  (See footnotes at end of Table).

| No | Site Name | Site Operator | Nature Reserve Status | Other air monitoring | Map Ref. | Type | Start | End |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 19 | Shetland | Met. Office |  | HNO3 NW, NO2 | hu500400 | D,F | Apr' 97 |  |
| 20 | Drayton | ADAS |  | ECN | sp162551 | D | Sep '96 |  |
| 21 | Glensaugh | MLURI |  | ECN / HNO3 NW | no664789 | D,F | Jun '97 |  |
| 22 | Moor House | CEH Lancaster | NNR | ECN / HNO3 NW | ny751334 | D,F | Sep '97 |  |
| 23 | North Wyke | IGER |  | ECN | sx659983 | D,F | Sep '96 |  |
| 24 | Rothamsted | IACR |  | ECN / HNO3 NW | tl123129 | D,F | Sep '96 |  |
| 25 | Sourhope | MLURI |  | ECN | nt867218 | D,F | May '97 |  |
| 26 | Wytham Woods | NERC/CEH | SSSI | ECN, HM | sp452083 | D | Sep '96 |  |
| 27 | Alice Holt | Forest Research |  | ECN | su809379 | D | Sep '96 |  |
| 28 | Porton Down | CBDE Porton | NNR | ECN | su253365 | D | Sep '96 | Nov ‘04 |
| 28B | Porton Down | CBDE Porton | NNR | ECN | su223384 | D | Jun ‘05 |  |
| 29* | LLydaw | CCW | NNR | ECN | sh695572 | D,F* | Apr '97 | Jul ‘04 |
| 29* | LLydaw | CCW | NNR | ECN | sh695572 | T | Mar '05 |  |
| 30 | Strathvaich Dam | Clover Environmental Research |  | Primary / HNO3 NW | nh348750 | D,F | Sep '96 |  |
| 31 | Eskdalemuir | Met. Office |  | Primary / HNO3 NW | nt235030 | D,F | Sep '96 |  |
| 32 | High Muffles | Forest Research | NNR | Primary / HNO3 NW | se776939 | D,F | Sep '96 |  |
| 33 | Stoke Ferry | Kings Lynn & W. Norfolk Bor. Council |  | NOx, SO2, HNO3 NW | tl700988 | D,F,T | Nov '96 |  |
| 34 | Yarner Wood | English Nature | NNR | Primary / HNO3 NW, HM | sx789788 | D,F | Sep '96 |  |
| 35 | Lullington Heath | English Nature | NNR | SO2, O3, NOx | tq538016 | D,F | Dec '96 |  |
| 36 | Bloomsbury | Stanger Science |  | SO2, O3, NOx | tq264789 | D | Mar '97 | Apr '97 |
| 36B | Victoria | CG Images |  | SO2, O3, NOx | tq291790 | D,F | Dec '97 | Dec '99 |
| 36C | Cromwell Rd | CG Images |  | HNO3 NW , SO2, O3, NOx | tq266791 | D,F | Dec '99 |  |
| 37 | Five Acres | Cornwall Wildlife Trust | LNR |  | sw794486 | D,F | Sep '96 | Dec ‘05 |
| 38 | Sheffield | Univ. Sheffield |  |  | sk332870 | D,F | Nov '96 |  |
| 38B | Sheffield 2 | Sheffield Museum |  |  | sk339873 | T | May ‘04 |  |
| 39 | Silsoe | Silsoe Estate |  |  | tl088356 | D,F | Sep '96 |  |
| 40 | Sutton Bonnington | Univ. Nottingham |  | SO2, HNO3, O3, NOx | sk505268 | D,F | Dec '96 |  |

* S29 Dyffryn Mymbyr: No Power to site since May 05, because of building work; currently using passive ALPHA samplers.

Table 1: List of sites in ammonia monitoring network (Jun 08) cont. (See footnotes at end of Table).

| No | Site Name | Site Operator | Nature Reserve Status | Other air monitoring | Map Ref. | Type | Start | End |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 41 | Lagganlia | CEH Banchory |  | HNO3 NW | nh856037 | D,F,T | Sep '96 |  |
| 42 | Castle Cary | Somerset Wildlife Trust | LNR |  | st609319 | D,F | Mar '97 |  |
| 43 | Tadcaster | Environment Agency |  |  | se452455 | D | Oct '96 |  |
| 44 | Hillsborough | DANI |  | ECN, HNO3 NW | ij243577 | D,F | Oct '96 |  |
| 45 | Lough Navar | DARDNI |  | Primary / HNO3 NW, HM | ih065545 | D,F | Oct '96 |  |
| 46 | Sibton | CG Images |  | SO2, O3, NOx | tm363722 | D, T | Feb '97 |  |
| 47 | Rum | Scot. Natural Heritage | NNR | HNO3 NW | nm408992 | D,F | Sep '96 |  |
| 48 | Wem Moss | Shropshire Wildlife Trust | NNR |  | sj473343 | T | Sep '96 |  |
| 49 | Frodsam | Cheshire Wildlife Trust | LNR |  | sj525795 | T | Sep '96 | Oct '98 |
| 50 | Swettenham Meadows | Cheshire Wildlife Trust | LNR |  | sj804674 | T | Sep '96 | Oct '98 |
| 51 | Wybunbury Moss | English Nature | SSSI / NNR |  | sj698502 | T | Nov '96 | Oct '98 |
| 52A | Fenn's Moss 1 | English Nature | NNR |  | sj490365 | T | Oct' 96 |  |
| 52B | Fenn's Moss 2 | English Nature | NNR |  | sj478368 | T | Oct '97 |  |
| 52C | Fenn's Moss 3 | English Nature | NNR |  | sj498378 | T | May ‘00 |  |
| 53 | Little Budworth | Manchester Metropolitan University | NNR | NOx, N Manipulation | sj584658 | T | Oct '96 |  |
| 54 | Bickerton Hill | Manchester Metropolitan University | NNR | NOx, N manipulation | sj498527 | T | Oct '96 |  |
| 55 | Ruabon | Manchester Metropolitan University | NNR | NOx, N manipulation | sj225489 | T | Nov '96 |  |
| 56 | Wardlow Hay Cop | Univ. Sheffield | NNR | NOx, N manipulation | sk177737 | T | Nov '96 |  |
| 57 | Stanford | Ministry of Defence | SSSI |  | tl858948 | T | Nov '96 | Feb ‘06 |
| 57B | Stanford 2 | Ministry of Defence | SSSI |  | tl836929 | T | Mar ‘04 |  |
| 58 | Redgrave and Lopham Fens | Suffolk Wildlife Trust | NNR |  | tm050797 | T | Dec '96 |  |
| 59 | Dunwich Heath | The National Trust | SSSI |  | tm470680 | T | Dec '96 |  |
| 60 | Edinburgh | Castlecliff Training Workshop |  |  | nt253734 | D,F | Oct '97 | Mar ‘02 |
| 60B | Edinburgh 2 | CEH Edinburgh |  | SO2 | nt263726 | D,F | Apr ‘02 | Dec ‘05 |
| 60C | Edinburgh St Leonards | Edinburgh Council |  | HNO3 NW, AURN | nt262731 | D,F | Jan ‘06 |  |
| 61 | Much Hoole | Leyland District Council |  |  | sd473231 | T | Mar '97 | Dec '01 |
| 62 | Midge Hall | Leyland District Council |  |  | sd508231 | T | Mar '97 | Dec '01 |
| 63 | Cardigan | Welsh Wildlife Centre | LNR / SSSI |  | sn185453 | D,F | Feb '97 |  |

Table 1: List of sites in ammonia monitoring network (Jun 08) cont. (See footnotes at end of Table).

| No | Site Name | Site Operator | Nature Reserve Status | Other air monitoring | Map Ref. | Type | Start | End |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 64 | Pen Y Garn | CEH Bangor ADAS Pwllpeiran |  | NO2, N manipulation (until 05) | sn798771 | T | Feb '97 |  |
| 65 | Allt a Mharcaidh | CEH Banchory | NNR | ECN | nh895024 | T | Apr '97 |  |
| 66 | Dennington | Suffolk Coastal District Council |  |  | tm276669 | T | Mar '97 |  |
| 67 | Fressingfield | Mid Suffolk District Council |  |  | tm261759 | T | Mar '97 |  |
| 68 | Bedingfield | Mid Suffolk District Council |  |  | tm173684 | T | Mar '97 |  |
| 70 | Cwmystwyth | ADAS |  | SO2 / HNO3 NW / HM | sn771742 | D,F | Feb '97 |  |
| 71 | Myerscough | Myerscough College |  |  | sd498399 | T | Sep '97 |  |
| 72 | Cardoun Burn | Freshwater Fisheries Laboratory |  | Freshwater monitoring | nx546658 | T | Apr '98 |  |
| 73 | Jenny Hurn | Powertech |  | SO2 | sk816986 | D,F | Nov '98 | Jan ‘01 |
| 73B | Marton | Powertech |  | SO2 | sk844819 | D,F | Mar ‘02 | Jan ‘06 |
| 74 | Carlisle | Environment Agency |  |  | ny468554 | D,F | Feb '99 |  |
| 75 | Westhay Moor | Somerset Wildlife Trust | LNR |  | st455440 | T | Feb '99 |  |
| 76 | Pointon | Environment Agency |  |  | tf128313 | D,F | Feb '99 |  |
| 76B | Pointon 2 | Environment Agency |  |  | tf128313 | T | Oct '99 | Mar ‘02 |
| 76C | Pointon 3 | Environment Agency |  |  | tf128313 | T | Mar '02 |  |
| 77 | Carradale | SEPA |  | HNO3 NW | nr798378 | D,F | Mar '99 |  |
| 78 | Auchincruive | SAC Auchincuive |  |  | ns379234 | D,F | Mar '99 |  |
| 78B | Auchincruive 2 | SAC Auchincuive |  |  | ns384229 | T | Mar '99 | Sep ‘01 |
| 78C | Auchincruive 3 | SAC Auchincuive |  |  | ns379234 | T | Nov '01 |  |
| 79 | Coleraine | University of Ulster |  |  | iC884211 | D,F | Nov '99 |  |
| 80 | Lyulphs Tower | The National Trust |  |  | ny403202 | D,F | Aug '99 |  |
| 81 | Pitmedden | The National Trust for Scotland |  |  | nj883278 | D | May '00 | Aug ‘02 |
| 82 | Brompton | K. Hardisty |  |  | se389988 | T | May '00 |  |
| 83 | Barcombe Mills | Southeast Waters |  | HNO3 NW | tq438149 | D,F | Apr '00 |  |
| 84 | Thursley Common | Imperial College | SSSi | N manipulation | su910404 | T | Jun '00 |  |
| 85 | Savarnake | TBF Forestry Advisory Services |  | Level II ICP | su055888 | T | Aug '00 | Dec ‘06 |
| 86 | Lakes | Forest Research |  | Level II ICP | sd337941 | T | Aug '00 |  |
| 87 | Thetford | Forest Research |  | Level II ICP | tl944841 | T | Aug '00 |  |

Table 1: List of sites in ammonia monitoring network (Apr 07) cont. (See footnotes at end of Table).

| No | Site Name | Site Operator | Nature Reserve Status | Other air monitoring | Map Ref. | Type | Start | End |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 88 | Sherwood | Forest Research |  | Level II ICP | sk163905 | T | Aug '00 | Aug ‘06 |
| 89 | Rannoch | Forest Research |  | Level II ICP | nn603533 | T | Aug '00 |  |
| 90 | Coalburn | Forest Research |  | Level II ICP | ny693782 | T | Aug '00 | Mar ‘07 |
| 91 | Tummel | Forest Research |  | Level II ICP | nn744611 | T | Aug '00 |  |
| 92 | Loch Awe * | Forest Research |  | Level II ICP | nm966115 | T | Aug '00 | Mar ’07 * |
| 93 | Llynn Brianne | Forest Research |  | Level II ICP | sn816484 | T | Aug '00 |  |
| 94 | Alice Holt (2) | Forest Research |  | Level II ICP | su805427 | T | Aug '00 |  |
| 95 | Glenshee Hotel | D. Cruar |  |  | no111699 | T | Feb '01 |  |
| 95 | Glenshee Hotel | D. Cruar |  |  | no111699 | D,F | Jul ‘06 |  |
| 96 | Oldmeldrum | A.G. Robertson |  |  | NJ832273 | T | Aug '02 |  |
| 97 | Detling | Maidstone Environmental Health |  | HNO3 NW, HM | TQ801597 | D,F | Feb ‘06 |  |
| 98 | Harwell | AEA Technology |  | HNO3 NW | su474863 | D,F | Apr ‘06 |  |
| 99 | Ladybower | Lancaster University |  | HNO3 NW | SK164892 | D,F | Jan ‘06 |  |
| 100 | Plas Y Brenin | CCW |  | HNO3 NW | sh716578 | D,F | May ‘06 |  |
| 102 | Caenby | West Lindsey District Council |  | HNO3 NW | SK993900 | D,F | Jan ‘06 |  |
| 103 | Goonhilly | British Telecom |  | HNO3 NW, Primary | SW723214 | D,F | Jan ‘06 |  |
| 104 | Hinderclay Fen | R. Langston | NNR |  | TM025787 | T | Jul ‘06 |  |
| 105 | Dyffryn Mymbyr | CCW | NNR | ECN | sh639551 | T | Jun ‘08 |  |

S90 Coalburn and S92 Loch Awe: Monitoring stopped in Mar 07 due to funding cuts to ICP-Level II work activities. *S92 Loch Awe: NH3 monitoring resumed in Jan08 after agreement from Forestry Commission. S105 Dyffryn Mymbyr (ECN site): monitoring commenced in Jun 08, following requests from CCW / ECN, to compare local variability in NH3 concentrations with nearby S29 Llydaw and S100 Plas Y Brenin.

Key:  NNR, National Nature Reserve; LNR, Local Nature Reserve; SSSI, Site of Special Scientific Interest; ECN, Environmental Change Network Terrestrial Site; Primary, Defra Primary wet deposition monitoring site; HNO3 NW, Nitric Acid monitoring Network; HM, Heavy Metals monitoring network; Level II ICP, Long-term forest monitoring; D, denuder sampler; F,  aerosol sampler; T,  diffusion tube sampler (Sep ’96 – Apr ’00) and ALPHA samplers (May ’00 – current).

During the course of running the network, a small number of sites have had to be moved due to local changes, in which case the new location is referred to as e.g. site 9B, site 36C. A number of sites were also closed down, whilst new sites were started to fill in key gaps in the national picture as agreed at different stages of the project. Other changes to sites in late 2005/early 2006 were made in order to accommodate the increase from 12 to 30 sites in the HNO3 monitoring network.

## Integration of the Nitric Acid Monitoring Network with the NAMN

The new expanded 30 site HNO3 Monitoring Network (operated by CEH under subcontract to AEA Technology for defra and the Devolved Administrations) is an integral part of the UK NAMN. An extension of the DELTA methodology is deployed at 30 DELTA sites to additionally sample gaseous HNO3, SO2, HCl and aerosol NO3-, SO42-, Cl-, plus base cations Na+, Ca2+ and Mg2+. The expansion of the Nitric Acid Network replaced the former SO2 network. Results from this network are reported separately under the Acid Deposition Monitoring contract.

# Sampling Methods

## Active sampling method: DELTA system

The DELTA (DEnuder for Long-Term Atmospheric) sampling system was developed for long-term sampling of ammonia and then later also extended to sample ammonium (Sutton et al. 2001). This diffusion denuder method permits the selective removal of gaseous NH3 on the denuders, with subsequent collection of particulate NH4+ on a downstream filter pack (Ferm 1979). The method is simple to deploy, using a small air pump and a gas meter to record sampled volume.

### Sampling train

The sampling train used in the CEH DELTA system is shown in Figure 2. To sample NH3, the glass denuder tubes are coated internally with acid. Citric acid, phosphorous acid or tartaric acid can all be used, but oxalic acid is generally avoided, because loss of the coating can occur during sampling owing to its high volatility, and the long sampling times (e.g. 1 month) used by the DELTA system. In the UK network the denuders are prepared with citric acid, which gives a visible layer of coating on the tubes, allowing a QA check on prepared denuder prior to exposure.  The post-denuder filter for the collection of ammonium aerosol is also coated with citric acid.

Figure 2: Sampling train for separation and collection of gaseous NH3 and aerosol NH4+ in the DELTA system.

To establish capture efficiency, the DELTA system uses 2 denuders in series for every sample. Two borosilicate glass denuders are connected in series as shown in Figure 2. To enable a fully developed laminar flow, a short 2.3 cm glass tube (not coated) of the same material is connected to the front end. An additional glass tube at the back end serves to prevent possible contamination of the second denuder during handling and sample changeover. At sites where sampling of ammonium aerosol is also made, this is achieved simply by the addition of a post-denuder filter pack with an acid impregnated filter. The different tube sections are joined by silicone tubing, and provided with two polyurethane caps for sealing before and after sampling. The two parts may be folded over, utilizing a silicone junction, during posting.

### Denuder extraction and chemical analysis

Exposed samples are posted back to CEH by the site operators and stored at 4(C until analysis. Denuders are extracted in 3 ml deionised water, while post denuder aerosol filters are extracted in 4 ml of deionised water. The extracted samples are analyzed for ammonium on the high sensitivity AMFIA system (AMmonia Flow Injection Analysis) which is an automated system developed at ECN, Petten, NL. AMFIA is based on the selective dialysis of ammonium across a membrane at high pH with subsequent analysis of conductivity. The calibration range normally used is 0 - 10 ppm (0.1 ppm, 1 ppm and 10 ppm calibration standards), and the QC's used are 0.2 ppm (low QC), 0.9 ppm (low QC), 2 ppm (high QC) and 9 ppm (high QC). It is sometimes necessary to dilute the extracted samples and to repeat the analysis where the sample concentration is outside the calibration range.

Monitoring of laboratory performance is through participation in the EMEP and WMO-GAW inter-comparison schemes for analytical laboratories. In July 2006, “FloRRia”, a second generation AMFIA system (built by Mechatronics, NL) was purchased and installed, which adds to the laboratory’s unique capability and expertise in ammonium analysis.

### Calculation of NH3 concentrations

The amount of NH3 collected (Q) on a denuder due to air sampling is given by:

Q = (ce – cb)*v										(1)

where ce is the liquid concentration of an exposed sample, cb is the liquid concentration of a blank sample and v is the liquid volume of the extraction solution.

The air concentrations ((a) of NH3 is then determined as:

(a = Q/V										(2)

where V is the volume of air sampled, which is found directly from the gas meter readings, and is typically 15 m3 per month.

The use of two denuders in series allow for the determination of capture efficiency, by comparing the amounts of ammonia in both. An infinite series correction factor, based on the capture efficiency, is applied for ammonia not captured. The corrected air concentration of NH3 ((a (corrected ammonia)) is then determined as:

((a (corrected ammonia)) =   (a (Denuder 1) * [1/(1-((a (Denuder 2) / (a (Denuder 1))]			(3)

At a typical capture efficiency of 90 % in the first denuder, the correction represents 1 % of the corrected air concentration. At 80 %, 75 % and 70 % capture, the correction amounts to 6 %, 11 % and 17 % of the total, respectively. Below 60 % capture efficiency, the correction amounts to greater than 50 % and should not be applied. The air concentration of NH3 is then determined as:

(a  =  (a (Denuder 1) + (a (Denuder 2)								(4)

### Calculation of NH4+ concentrations

The air concentration ((a) of NH4+ from filter pack sampling is determined according to equations 1 and 2 described in section 3.1.3.

The calculated air concentrations ((a) of NH4+ is also corrected for ammonium which is due to incomplete capture of air NH3 by the double denuder. The corrected air concentrations ((a (corrected ammonium)) of NH4+ is then determined as:

(a (corrected ammonium) = (a (NH4+) – [((a (corrected ammonia) – ((a (Denuder 1) + (a (Denuder 2))]	(5)

Loss of NH3 due to volatilisation of NH4+ from the filter paper has been investigated, by adding a 3rd citric acid coated denuder after the filter pack, and was found to be negligible.

## Passive Diffusion Samplers

In the first phase of the network, the performance of 35 mm path length membrane diffusion tube was improved to permit reliable monthly measurements down to a level of c. 1 g m-3 (Sutton et al. 2001b). In the second phase of the network, an improved high sensitivity passive method, the CEH ALPHA (Adapted Low-cost Passive High Absorption) sampler with 6 mm path length was applied in the network (Figure 3, Tang et al. 2001b). Compared with the diffusion tube sampler, the ALPHA method shows an improvement of precision and detection limits by a factor of ~20. Combined with careful attention to analytical procedures, replication and ongoing calibration against the DELTA system, the detection limit of the ALPHA sampler for monthly sampling of NH3 is around 0.02 g m-3. In May 2000, the diffusion tube method was replaced by the new improved ALPHA sampler across the NAMN.

Figure 3: Diagram of a single CEH ALPHA sampler for NH3, which has an optimized design to meet both sampling and operational criteria.

The passive sampling system consists of three replicate ALPHA samplers attached by the use of velcro to an aerodynamically shaped support (upturned frisbee or plant saucer) on a pole or post at about 1.5 m height above ground. Triplicate samplers are implemented at each site in order to give a more reliable estimation of the air concentration of ammonia.

### Analysis of passive samplers

Exposed samples are returned to CEH by post and stored at 4(C until analysis.  Samples are extracted into deionised water and analysed for ammonium on the AMFIA system (see section 3.1.2).

### Calculation of NH3 concentrations

All passive samplers operate on the principle of diffusion of gases from the atmosphere along a sampler of defined dimensions onto an absorbing medium, according to Fick’s law. The theoretical uptake rate of a sampler is a function of the length, L (m) and the cross sectional area, A (m2) of the stationary air layer within the sampler, and can be calculated provided that the diffusion coefficient, D (m2 s-1) of the gas of interest is known. The diffusion path length is nominally the distance from the mouth of the sampler to the reaction surface at the other end of the tube. Disturbance to the stationary air layer, such as through the effect of wind turbulence, can shorten the nominal path length. Conversely, the use of a turbulence-damping membrane at the inlet can increase the effective path length due to a quasi-laminar layer of air forming adjacent to the outside of the membrane.

The effective volume of air sampled (V, m3) by the CEH ALPHA sampler is given by:

V = DAt/L		(1)

where t = time of exposure  (h)	D = 2.09 x 10-5 m2 s-1 at 10(C

A = 3.4636 x 10-4 m2

L = 0.006 m

V (m3) = 0.004343362 m3 x t (h)	(2)

The air concentration of a pollutant ((, e.g. g m-3) can then be calculated as:

( = (me – mb) / V	(3)

Where	me = amount of NH3 collected on an exposed sample (e.g. g)

mb = amount of NH3 in the blank sample  (e.g. g)

### Calibration of passive samplers

Both the ALPHA sampler and the membrane diffusion tube have a gas permeable membrane placed at the inlet to establish a turbulent free layer of air inside the sampler. The membrane and overlying laminar boundary layer of air do however impose an additional resistance against gas diffusion, which needs to be taken into account when deriving the sampler’s effective sampling rate. This may be achieved by applying a correction to the measured concentration using the theoretical rate. This is determined empirically from field calibration of the samplers against the reference DELTA system at 12 sites in the network where the 2 methods are implemented in parallel on a long-term basis.

## Quality Assurance and Quality Control of sampling methods

This section describes the main QA and QC approaches used in the UK network (Tang & Sutton 2003). QA of the network is maintained through careful adherence to specific written sampling protocols of good laboratory and site operator practice. In addition to the QA measures which maximise the quality of the data collected, a number of QC criteria are also applied to screen the collected dataset. Data passing and failing the QC thresholds can then be compared to identify any biases. Two levels of data filtration are provided:

1. Standard data filtration

DELTA system: two denuders in series are used for every sample to check capture efficiency for NH3: distinction is made between samples providing ( 75% of the total NH3 captured in the first of the two denuders, compared with < 75% of the total capture being in the first denuder. Values less than this indicate an imperfectly coated acid film or some other sampling problems and it cannot then be guaranteed that all the NH3 is captured in both denuders. It should be noted that a collection efficiency correction is applied to the measurement based on the capture efficiency (Sutton et al. 2001a, 2001b). Gas meter flow rates are also monitored. The air pumps used are relatively stable, at 0.25 – 0.4 l min-1, and data fail the QC standard where the air sampling rate for a sampling period is < 0.23 l min-1. Low measured flow rates indicate that the pump may need oiling, that an extended power cut has occurred or that there is a leak in the system. Any low flow rate for a month is investigated promptly with the site operator.

Passive samplers (ALPHA samplers): replicate samples (at least 3) are used at every site to provide estimates of precision of the method, and to identify contamination artefacts. Where the % coefficient of variation (CV = standard deviation / mean) of the replicate samplers is greater than 30% for diffusion tube samplers, and 15 % for ALPHA samplers, the sample run is classed as failing the QC test. Large discrepancies greater than the set quality standard are most likely due to contamination of samples.

2. Manual screening of outliers

In addition to the above tests, the full dataset is investigated for outliers in relation to the functioning of the equipment.  This is designed to identify the small number of runs where there was clearly a sampling malfunction. This exclusion includes such events as vandalized samples, water ingress and invasion by invertebrates.

# Results and Discussion

## Performance of the network

(A)

(B)

Figure 4: A) Total data capture of the NAMN. The total number of measurements is currently around 12 larger than the total number of sites in the network due to replicated measurement by more than one method at certain sites, and B) % of data passing the QC thresholds (DELTA: capture of NH3 ( 75 % in the first of the 2 denuders, flow rate = > 0.22 L min-1; DT/ALPHA: % CV for replicate samples < 30 % and < 15 % respectively. The decrease in % data capture in 1997 was due to ageing of denuders (the protocol was improved), while the effect of Foot and Mouth Disease in 2001 can be clearly seen as a decrease in the number of measurements providing data.

In Figure 4, the number of measurements obtained for each month is compared with the percentage of samples passing the QC thresholds. The number of measurements is greater than the number of monitoring sites in the network, because of the parallel application of more than one method at several sites. The decrease in % data capture in 1997 was due to imperfect coating of denuders (the denuder coating protocol was subsequently improved), whilst the dips in the spring of 1998 and 1999 were attributed to high temperatures in monitoring cabin housing the DELTA equipment which affect NH3 sampling (this was improved through providing increased ventilation and in some cases, moving the DELTA sampling equipment to an outdoor location). Since these changes, the passing of the QC criteria has been consistently better than 80 %.

## Measurement reproducibility

The quality/precision of the measurement data using DELTA sampling can be demonstrated at a selected number of sites where replicated sampling has been applied.  This is shown for example for Bush OTC (S1), near CEH Edinburgh, in Figure 5.

Figure 5: At the Bush OTC site in Scotland (S1 Bush OTC: mixed agricultural area, NT243642), two DELTA systems are operated in parallel to provide an ongoing assessment of the precision of the DELTA approach. Excellent agreement was achieved with the replicate sampling (e.g. an annual average difference of ( 2 % in NH3, and ( 2 % in NH4+).

Replicated sampling at Bush OTC (S1) illustrates the precision of the DELTA approach (< 10 % in individual monthly values), and an annual average difference within ( 2 %. The overall mean of all data was 2.17 g NH3 m-3, compared to 2.16 g NH3 m-3 using only the filtered data. Inclusion of data failing the criterion of >75% capture in the first denuder therefore does not appear to present a bias in the long-term dataset. The monitored mean concentration is also similar to the FRAME predicted concentration (2.08 g NH3 m-3 from FRAME 5.05, 2002 emissions data, 1.59 g NH3 m-3 from FRAME 6.12, 2005 emissions data) for the 5 km grid square (Singles et al, 1998, Fournier et al 2002, Dore et al. 2006), whilst the mean aerosol NH4+ concentration of 0.77 g NH4+ m-3 is higher than compared with FRAME estimates (0.32 g NH4+ m-3 from FRAME 5.05, 2002 emissions, 0.51 g NH4+ m-3 from FRAME 6.12, 2005 emissions). The changes in modelled NH4+ concentration are due to both reduced SO2 and NOx emissions and model changes.

Figure 6: Correlation plots of replicate DELTA measurements made at Bush OTC (NT243642).

The seasonal pattern at Bush OTC, with spring and autumn peaks in NH3 matches the times when manure would be applied to agricultural fields, plus emissions from grazing animals over the summer months. Inter-annual differences can also be seen, with larger NH3 concentrations in 2001 and 2003, reflecting warmer drier summers, while the peak NH4+ concentration in Spring 2003 reflects polluted, continental air masses during this period. High concentrations of aerosol and acid gases were seen at most UK sites for these months in the UK HNO3 network (Tang et al. 2007).

## Intercomparison of delta and passive sampling methods

Results from the comparison of the ALPHA samplers against the DELTA system at intercomparison sites across the UK are used to derive an effective uptake rate for the ALPHA sampler. In addition, parallel measurements with the DELTA and ALPHA are also made at a farm site with high NH3 concentrations near S1 Bush OTC, in order to extend the calibration range, and also to ascertain linearity of response which is very important. The calibration is necessary to account for the fact that the diffusion path length of the passive sampler is slightly longer than the distance between the membrane and adsorbent, due to the presence of a laminar boundary layer resistance at the membrane inlet of the sampler plus the additional resistance to diffusion through the turbulence damping membrane.

Since February 2007, a new PTFE membrane (Swiftlab 07-OPM-027) has been implemented with the ALPHA samplers, which replaced the previous PTFE membrane (TE38) from Schleicher & Schuell (now part of Whatman). The physical characteristics of the two membranes are compared in

Table 2. Since the Swiftlab membrane is thicker, it is expected that the sampling rate will change. Since the Swiftlab membrane is supported on a regular polypropylene grid, it has an even thickness across the membrane, compared with the TE38.

Table 2: Comparison of TE38 and Swiftlab PTFE membranes.

|  | TE38 PTFE membrane | New PTFE membrane (Swiftlab) |
| --- | --- | --- |
| Size | 27 mm diameter | 27 mm diameter |
| Porosity | 5 um pore size | 5 um pore size |
| Thickness | 265 µm | 305 µm |
| Support material | Randomly arranged polypropylene support material | Regular Polypropylene grid |

Based on field calibration against the DELTA system (Figure 7), the membrane resistance (Swiftlab PTFE membrane) equated to an extra 2 mm path length from the 2007 calibration.

Effective uptake rate (Swiftlab PTFE membrane), V (m3) = 0.003241315 m3 x t (h)	(4)

By comparison, the TE38 membrane equated to an extra 0.83 mm path length from past calibrations.

Effective uptake rate (with TE38 membrane, 2006), V (m3) = 0.003787816 m3 x t (h)	  (5)

Figure 7: Regression of ALPHA vs DELTA used to derive an effective uptake rate for the ALPHA samplers. Data shown are the period Feb-07 – Jan08.

The annual regressions are used to calibrate the diffusion tube and ALPHA sampler and data, which are mapped together with the data for active denuder sampling. To ensure that bias is not introduced in the sampling and to maintain the validity of long-term trends, the calibration is analysed on an annual basis as a check that the passive samplers in relation to the DELTA does not deviate significantly with time.

Figure 9: compares the annual empirical calibration for the passive samplers, based on their theoretical sampling rate (not including any membrane or boundary layer resistance) against the reference DELTA method. There is no systematic trend over time in either of the passive method calibrations. The annual calibration functions of both the diffusion tubes and ALPHA samplers show both high precision and constancy between years. This is very important, as it lends support for the detection of temporal trends in ammonia concentrations. The mean diffusion tube calibration (at 10 g m-3) amounts to a correction of 2.8% compared with the DELTA system, with the standard deviation of the different annual calibrations being 3.8%. The mean ALPHA calibration (at 10 g m-3) amounts to a correction of 10 % (ALP1: ALPHA sampler type 1), 11 % (ALP2 + ALP3: ALPHA samplers type 2 and 3) and 13 % (ALP3M: ALPHA samplers type 3 with Swiftlab PTFE membrane) respectively, compared with the DELTA system, with the standard deviation of the different annual calibrations being < 1%.

Figure 8: Comparison of annual empirical calibration curves for the Diffusion Tubes against the reference estimates from DELTA sampling at 10 sites in the UK NAMN.

Figure 9: Comparison of annual empirical calibration curves for the ALPHA samplers against the reference estimates from DELTA sampling at 12 sites in the UK National Ammonia Monitoring Network. ALP1 is the first prototype ALPHA sampler that was made with a 22 mm diameter exposure surface (1998-2000), while ALP2 (2001-2005) and ALP3 (2006 to present) were produced commercially from injection moulding with a 21 mm diameter exposure surface. TE38 PTFE membrane was used throughout the whole period, but was replaced with the new Swiftlab PTFE membrane from Feb 07.

## Summary of measurements

Monitored mean 2007 annual concentrations of gaseous NH3 and particulate NH4+ at individual sites in the network are compared in Figure 10 and Figure 11.

Figure 10: Mean monitored concentrations of gaseous NH3 at individual sites in the NAMN. Each data point represents the annual mean concentrations of monthly measurements made at each site in 2007, whilst the bars show the minimum and maximum concentrations observed. Key:  D = DELTA sampler, T = ALPHA samplers.

The largest NH3 concentrations occurred at sites that are in regions with high ammonia emissions, e.g. S68 Fressingfield in East Anglia (pig & poultry emissions); 2007 annual mean of = 7.9 µg NH3 m-3, range = 2.8 – 22 µg NH3 m-3. The smallest NH3 concentrations were observed at remote sites locations that are located in less populated areas, and with few ammonia emission sources, e.g. S3 Inverpolly, S30 Strathvaich Dam in Northern Scotland. For particulate NH4+, the annual mean concentrations ranged from 0.16 to 1.5 µg NH4+ m-3.

Figure 11: Mean monitored annual concentrations of particulate NH4+ at individual sites in the NAMN. Each data point represents the annual mean concentrations of monthly measurements made at each site in 2007, whilst the bars show the minimum and maximum concentrations observed.

Statistical summaries of the measurements made in 2007 of gaseous NH3 and aerosol NH4+ are given in. The complete set of the monthly measurements made in 2007 can be found in the Appendix.

Table 3: Summary of statistics for monthly measurements in 2007.

|  |  |  | Gaseous NH3 | Particulate NH4+ |
| --- | --- | --- | --- | --- |
| No. | Name | Method | Mean | Min | Max | SD | CV (%) | N | Mean | Min | Max | SD | CV (%) | N |
| 1 | Bush OTC-LHS | D | 1.62 | 1.05 | 2.64 | 0.50 | 30.6 | 12 | 0.57 | 0.13 | 1.12 | 0.37 | 65.5 | 12 |
| 1 | Bush OTC-RHS | D | 1.65 | 0.98 | 2.74 | 0.48 | 29.1 | 12 | 0.58 | 0.13 | 1.13 | 0.37 | 63.6 | 12 |
| 1 | Bush OTC | B | 1.60 | 0.96 | 2.80 | 0.51 | 31.9 | 12 |  |  |  |  |  |  |
| 2 | Bush Cabin | B | 0.79 | 0.39 | 1.40 | 0.28 | 35.7 | 12 |  |  |  |  |  |  |
| 3B | Inverpolly 2 (met enc.) | D | 0.06 | 0.02 | 0.17 | 0.04 | 71.2 | 12 | 0.17 | 0.01 | 0.44 | 0.14 | 80.2 | 12 |
| 3B | Inverpolly 2 (met enc.) | B |  |  |  |  |  |  |  |  |  |  |  |  |
| 4 | Penallt | D | 2.16 | 0.61 | 8.56 | 2.28 | 105.4 | 12 |  |  |  |  |  |  |
| 6B | Rosemaund | D | 3.44 | 1.39 | 10.54 | 2.56 | 74.3 | 12 | 1.10 | 0.16 | 2.39 | 0.77 | 70.1 | 12 |
| 8C | Narberth | D | 1.70 | 0.16 | 5.58 | 1.42 | 83.4 | 11 | 1.51 | 0.33 | 5.99 | 1.64 | 108.0 | 11 |
| 9B | Brown Moss NR 2 | D | 3.03 | 1.43 | 9.10 | 2.11 | 69.6 | 12 |  |  |  |  |  |  |
| 9B | Brown Moss NR 2 | B | 2.58 | 1.45 | 5.35 | 1.21 | 47.1 | 11 |  |  |  |  |  |  |
| 10 | Bure Marshes | D | 1.08 | 0.36 | 2.13 | 0.57 | 52.4 | 12 |  |  |  |  |  |  |
| 11 | Mere Sands Wood | D | 1.48 | 0.52 | 3.19 | 0.75 | 50.9 | 11 | 0.95 | 0.25 | 3.63 | 0.91 | 95.3 | 12 |
| 11 | Mere Sands Wood | B | 1.54 | 0.83 | 3.51 | 0.82 | 53.0 | 12 |  |  |  |  |  |  |
| 12 | Halladale | D | 0.51 | 0.14 | 1.09 | 0.30 | 59.9 | 11 | 0.20 | 0.03 | 0.49 | 0.13 | 65.4 | 11 |
| 13 | Aston Rowant. | D | 2.49 | 0.29 | 10.18 | 2.87 | 115.4 | 12 |  |  |  |  |  |  |
| 14 | Ellon Ythan | D | 5.54 | 1.64 | 14.14 | 3.94 | 71.1 | 10 |  |  |  |  |  |  |
| 15 | Llynclys Common | D | 1.58 | 0.86 | 3.63 | 0.71 | 44.8 | 12 |  |  |  |  |  |  |
| 15 | Llynclys Common | B | 1.46 | 0.69 | 3.53 | 0.71 | 48.9 | 12 |  |  |  |  |  |  |
| 16 | Northallerton | D | 3.99 | 1.44 | 6.09 | 1.76 | 44.2 | 12 | 1.12 | 0.30 | 2.30 | 0.71 | 63.5 | 12 |
| 17 | Easingwold | D | 1.52 | 0.10 | 5.40 | 1.43 | 94.3 | 11 | 1.27 | 0.32 | 2.91 | 0.90 | 70.6 | 11 |
| 18 | Auchencorth Moss | LHS D | 0.78 | 0.48 | 1.48 | 0.31 | 40.1 | 12 | 0.54 | 0.11 | 1.25 | 0.37 | 68.5 | 12 |
| 18 | Auchencorth Moss | RHS D | 0.68 | 0.41 | 1.32 | 0.28 | 41.6 | 12 | 0.48 | 0.11 | 1.08 | 0.31 | 64.7 | 12 |
| 18 | Auchencorth Moss | B | 0.77 | 0.41 | 1.49 | 0.35 | 45.6 | 11 |  |  |  |  |  |  |
| 19 | Shetland | D | 0.13 | 0.04 | 0.21 | 0.05 | 40.0 | 11 | 0.29 | 0.03 | 0.62 | 0.19 | 66.7 | 11 |
| 20 | Drayton | D | 1.75 | 0.66 | 4.87 | 1.21 | 69.3 | 12 |  |  |  |  |  |  |
| 21 | Glensaugh | D | 0.31 | 0.15 | 0.67 | 0.14 | 44.8 | 12 | 0.41 | 0.08 | 0.95 | 0.29 | 71.7 | 12 |
| 21 | Glensaugh | B | 0.22 | 0.10 | 0.52 | 0.12 | 54.2 | 11 |  |  |  |  |  |  |
| 22 | Moor House | D | 0.42 | 0.16 | 0.92 | 0.20 | 48.4 | 11 | 0.57 | 0.14 | 1.38 | 0.37 | 64.3 | 11 |
| 22 | Moor House | B | 0.37 | 0.09 | 0.70 | 0.17 | 45.2 | 12 |  |  |  |  |  |  |
| 23 | North Wyke | D | 2.07 | 0.64 | 4.47 | 1.09 | 52.6 | 12 | 0.75 | 0.21 | 2.39 | 0.60 | 79.3 | 12 |
| 24 | Rothamsted | D | 1.32 | 0.45 | 4.28 | 1.08 | 81.9 | 11 | 1.39 | 0.53 | 2.75 | 0.81 | 58.4 | 11 |
| 25 | Sourhope | D | 0.44 | 0.22 | 0.69 | 0.18 | 40.4 | 10 | 0.35 | 0.10 | 0.73 | 0.24 | 66.6 | 9 |
| 25 | Sourhope | B | 0.36 | 0.09 | 0.75 | 0.19 | 52.3 | 11 |  |  |  |  |  |  |
| 26 | Wytham Woods | D | 1.29 | 0.52 | 4.06 | 0.94 | 72.9 | 12 |  |  |  |  |  |  |
| 27 | Alice Holt | D | 1.53 | 0.48 | 3.56 | 1.11 | 72.9 | 8 |  |  |  |  |  |  |
| 28 | Porton Down | D | 1.73 | 0.66 | 6.24 | 1.54 | 88.7 | 12 |  |  |  |  |  |  |
| 29 | Llydaw | B | 5.87 | 1.86 | 16.73 | 5.08 | 86.6 | 12 |  |  |  |  |  |  |
| 30 | Strathvaich Dam | D | 0.10 | 0.05 | 0.28 | 0.06 | 66.7 | 12 | 0.16 | 0.03 | 0.62 | 0.16 | 103.2 | 11 |
| 31 | Eskdalemuir | D | 0.37 | 0.18 | 0.76 | 0.17 | 45.2 | 12 | 0.54 | 0.15 | 1.08 | 0.33 | 61.2 | 12 |
| 32 | High Muffles | D | 0.63 | 0.27 | 1.68 | 0.36 | 56.5 | 12 | 0.83 | 0.30 | 1.50 | 0.44 | 52.4 | 12 |
| 33 | Stoke Ferry | D | 2.70 | 1.48 | 6.62 | 1.37 | 50.7 | 12 | 1.31 | 0.40 | 2.91 | 0.70 | 53.6 | 12 |
| 33 | Stoke Ferry | B | 2.62 | 1.32 | 6.47 | 1.37 | 52.2 | 12 |  |  |  |  |  |  |
| 34 | Yarner Wood | D | 0.56 | 0.20 | 1.93 | 0.48 | 86.3 | 12 | 0.93 | 0.25 | 3.58 | 0.90 | 96.6 | 12 |
| 35 | Lullington Heath | D | 0.60 | 0.25 | 2.44 | 0.60 | 100.7 | 12 | 0.92 | 0.42 | 2.28 | 0.61 | 66.1 | 12 |

Table 3: Summary of statistics for monthly measurements in 2007. (cont.)

|  |  |  | Gaseous NH3 | Aerosol NH4+ |
| --- | --- | --- | --- | --- |
| No. | Name | Method | Mean | Min | Max | SD | CV (%) | N | Mean | Min | Max | SD | CV (%) | N |
| 36c | London Cromwell rd | D | 4.01 | 2.50 | 7.48 | 1.22 | 30.3 | 12 | 1.54 | 0.69 | 3.04 | 0.70 | 45.2 | 12 |
| 38 | Sheffield | D | 0.67 | 0.12 | 1.50 | 0.37 | 54.9 | 12 | 1.05 | 0.35 | 2.99 | 0.71 | 68.3 | 12 |
| 38B | Sheffield 2 | B | 1.52 | 1.01 | 2.63 | 0.46 | 30.2 | 12 |  |  |  |  |  |  |
| 39 | Silsoe | D | 1.66 | 0.62 | 3.91 | 0.96 | 57.8 | 12 | 1.27 | 0.48 | 3.04 | 0.76 | 60.1 | 12 |
| 39 | Silsoe | B | 1.76 | 0.56 | 4.77 | 1.12 | 63.7 | 12 |  |  |  |  |  |  |
| 40 | Sutton Bonington | D | 4.15 | 1.33 | 9.48 | 2.45 | 58.9 | 12 | 1.31 | 0.58 | 2.60 | 0.67 | 50.7 | 12 |
| 41 | Lagganlia | D | 0.58 | 0.10 | 2.02 | 0.56 | 97.1 | 12 | 0.31 | 0.07 | 1.06 | 0.29 | 92.3 | 12 |
| 41 | Lagganlia | B | 0.51 | 0.08 | 1.88 | 0.55 | 107.5 | 12 |  |  |  |  |  |  |
| 42 | Castle Cary | D | 4.34 | 2.53 | 7.68 | 1.51 | 34.7 | 12 | 0.87 | 0.35 | 1.75 | 0.46 | 53.1 | 12 |
| 43 | Tadcaster | D | 1.95 | 0.64 | 5.38 | 1.22 | 63.0 | 12 |  |  |  |  |  |  |
| 44 | Hillsborough | D | 3.91 | 1.74 | 7.98 | 2.18 | 55.7 | 12 | 0.66 | 0.22 | 2.05 | 0.51 | 77.0 | 12 |
| 45 | Lough Navar | D | 0.70 | 0.19 | 2.04 | 0.54 | 77.3 | 12 | 0.45 | 0.08 | 1.06 | 0.34 | 75.3 | 12 |
| 46 | Sibton | D | 1.43 | 0.46 | 4.34 | 1.08 | 75.5 | 12 |  |  |  |  |  |  |
| 46 | Sibton | B | 2.14 | 0.83 | 5.63 | 1.32 | 61.5 | 12 |  |  |  |  |  |  |
| 47 | Rum | D | 0.32 | 0.10 | 0.82 | 0.20 | 62.0 | 11 | 0.25 | 0.08 | 0.62 | 0.17 | 64.9 | 11 |
| 48 | Wem Moss | B | 2.06 | 0.90 | 4.16 | 1.14 | 55.5 | 12 |  |  |  |  |  |  |
| 52A | Fenn's Moss | B | 2.31 | 1.01 | 5.30 | 1.23 | 53.3 | 12 |  |  |  |  |  |  |
| 52B | Fenn's Moss 2 | B | 1.94 | 0.96 | 4.45 | 0.94 | 48.4 | 12 |  |  |  |  |  |  |
| 52C | Fenn's Moss 3 | B | 3.46 | 1.14 | 8.30 | 2.49 | 71.9 | 12 |  |  |  |  |  |  |
| 53 | Little Budworth | B | 2.68 | 0.73 | 9.63 | 2.43 | 90.7 | 12 |  |  |  |  |  |  |
| 54 | Bickerton HIll | B | 2.77 | 1.41 | 7.64 | 1.70 | 61.4 | 12 |  |  |  |  |  |  |
| 55 | Ruabon | B | 0.67 | 0.22 | 1.39 | 0.55 | 81.8 | 9 |  |  |  |  |  |  |
| 56 | Wardlow Hay Cop | B | 1.14 | 0.45 | 2.73 | 0.61 | 53.9 | 11 |  |  |  |  |  |  |
| 57 | Stanford | B |  |  |  |  |  |  |  |  |  |  |  |  |
| 57B | Stanford 2 | B | 1.77 | 0.47 | 3.32 | 0.87 | 49.2 | 12 |  |  |  |  |  |  |
| 58 | Redgrave+ Lopham | B | 3.19 | 1.15 | 13.82 | 3.55 | 111.3 | 12 |  |  |  |  |  |  |
| 59 | Dunwich Heath | B | 0.86 | 0.34 | 1.68 | 0.48 | 55.3 | 11 |  |  |  |  |  |  |
| 60C | Edin. St Leonards | D | 1.33 | 0.80 | 1.83 | 0.31 | 23.2 | 12 | 0.71 | 0.25 | 1.36 | 0.43 | 61.5 | 12 |
| 63 | Cardigan | D | 0.78 | 0.29 | 1.72 | 0.45 | 58.1 | 8 |  |  |  |  |  |  |
| 64 | Pwllpeiran | B | 0.39 | -0.01 | 1.95 | 0.54 | 139.6 | 12 |  |  |  |  |  |  |
| 65 | Allt a Mharcaidh | B | 0.18 | 0.02 | 1.12 | 0.31 | 171.4 | 12 |  |  |  |  |  |  |
| 66 | Dennington | B | 3.24 | 0.81 | 8.52 | 2.51 | 77.7 | 12 |  |  |  |  |  |  |
| 67 | Fressingfield | B | 6.27 | 2.35 | 14.46 | 3.83 | 61.0 | 12 |  |  |  |  |  |  |
| 68 | Bedlingfield | B | 7.85 | 2.76 | 21.57 | 5.93 | 75.5 | 12 |  |  |  |  |  |  |
| 70 | Cwmystwyth | D | 2.10 | 0.40 | 4.78 | 1.29 | 61.1 | 12 | 0.73 | 0.24 | 1.66 | 0.48 | 65.3 | 12 |
| 71 | Myerscough | B | 4.76 | 2.68 | 14.22 | 3.14 | 65.9 | 12 |  |  |  |  |  |  |
| 72 | Cardoun Burn | B | 0.27 | 0.05 | 1.00 | 0.26 | 94.9 | 12 |  |  |  |  |  |  |
| 74 | Carlisle | D | 3.64 | 2.21 | 6.00 | 1.24 | 34.1 | 11 | 0.62 | 0.14 | 1.23 | 0.37 | 60.1 | 11 |
| 75 | Westhay Moor | B | 1.38 | 0.23 | 3.40 | 0.84 | 60.8 | 11 |  |  |  |  |  |  |
| 76 | Pointon | D | 7.03 | 2.05 | 14.14 | 3.65 | 52.0 | 12 | 1.30 | 0.07 | 3.75 | 1.09 | 83.5 | 12 |
| 76C | Pointon 3 | B | 2.61 | 0.62 | 9.61 | 2.33 | 89.3 | 12 |  |  |  |  |  |  |
| 77 | Carradale | D | 1.13 | 0.36 | 2.30 | 0.64 | 56.6 | 12 | 0.38 | 0.10 | 1.09 | 0.29 | 76.7 | 11 |
| 78 | Auchincruive | D | 9.28 | 1.86 | 15.85 | 4.45 | 48.0 | 12 | 0.54 | 0.09 | 0.93 | 0.31 | 57.1 | 12 |
| 78C | Auchincruive 3 | B | 5.22 | 1.44 | 10.13 | 2.71 | 52.0 | 12 |  |  |  |  |  |  |
| 79 | Coleraine | D | 2.90 | 2.01 | 5.85 | 1.15 | 39.6 | 11 | 0.43 | 0.16 | 0.85 | 0.22 | 50.8 | 11 |

Table 3: Summary of statistics for monthly measurements in 2007. (cont.)

|  |  |  | Gaseous NH3 | Aerosol NH4+ |
| --- | --- | --- | --- | --- |
| No. | Name | Method | Mean | Min | Max | SD | CV (%) | N | Mean | Min | Max | SD | CV (%) | N |
| 80 | Lyulphs Tower | D | 0.88 | 0.18 | 4.30 | 1.11 | 125.9 | 12 | 0.44 | 0.09 | 0.93 | 0.27 | 62.3 | 12 |
| 82 | Brompton | B | 5.60 | 2.15 | 12.08 | 2.99 | 53.3 | 12 |  |  |  |  |  |  |
| 83 | Barcombe Mills | D | 1.41 | 0.49 | 3.78 | 1.04 | 73.4 | 12 | 1.32 | 0.59 | 3.30 | 0.77 | 58.2 | 11 |
| 84 | Thursley Common | B | 0.68 | 0.20 | 2.62 | 0.64 | 95.0 | 12 |  |  |  |  |  |  |
| 85 | Savarnake | B |  |  |  |  |  |  |  |  |  |  |  |  |
| 86 | Lakes | B | 0.88 | 0.33 | 2.61 | 0.63 | 71.1 | 12 |  |  |  |  |  |  |
| 87 | Thetford | B | 1.75 | 0.99 | 3.38 | 0.88 | 50.3 | 12 |  |  |  |  |  |  |
| 88 | Sherwood | B |  |  |  |  |  |  |  |  |  |  |  |  |
| 89 | Rannoch | B | 0.04 | 0.00 | 0.15 | 0.04 | 115.6 | 12 |  |  |  |  |  |  |
| 90 | Coalburn | B | 0.27 | 0.14 | 0.34 | 0.11 | 40.6 | 3 |  |  |  |  |  |  |
| 91 | Tummel | B | 0.05 | 0.01 | 0.18 | 0.05 | 96.8 | 12 |  |  |  |  |  |  |
| 92 | Loch Awe | B | 0.05 | 0.03 | 0.07 | 0.02 | 47.4 | 3 |  |  |  |  |  |  |
| 93 | Llynn Brianne | B | 0.18 | 0.06 | 0.48 | 0.15 | 85.2 | 11 |  |  |  |  |  |  |
| 94 | Alice Holt (2) | B | 0.66 | 0.23 | 2.02 | 0.55 | 83.7 | 12 |  |  |  |  |  |  |
| 95 | Glenshee Hotel | D | 0.54 | 0.20 | 1.19 | 0.30 | 55.2 | 11 |  |  |  |  |  |  |
| 95 | Glenshee Hotel | B | 0.35 | 0.07 | 0.76 | 0.22 | 63.3 | 12 |  |  |  |  |  |  |
| 96 | Oldmedrum | B | 1.10 | 0.69 | 1.86 | 0.36 | 32.9 | 12 |  |  |  |  |  |  |
| 97 | Rochester | D | 2.67 | 0.57 | 8.54 | 2.81 | 105.3 | 12 | 1.16 | 0.36 | 2.14 | 0.55 | 46.9 | 12 |
| 98 | Harwell | D | 1.81 | 0.49 | 4.83 | 1.12 | 62.0 | 12 | 1.27 | 0.47 | 2.82 | 0.75 | 59.6 | 11 |
| 99 | Ladybower | D | 0.76 | 0.35 | 1.52 | 0.32 | 42.1 | 12 | 0.99 | 0.37 | 2.46 | 0.67 | 66.9 | 12 |
| 100 | Plas Y Brenin | D | 0.42 | 0.14 | 1.34 | 0.32 | 75.1 | 12 | 0.62 | 0.13 | 1.66 | 0.43 | 69.7 | 12 |
| 102 | Caenby | D | 3.00 | 0.90 | 10.34 | 2.61 | 87.1 | 11 | 1.10 | 0.62 | 1.91 | 0.49 | 44.9 | 11 |
| 103 | Goonhilly | D | 0.63 | 0.20 | 1.40 | 0.32 | 51.4 | 12 | 0.79 | 0.30 | 2.88 | 0.81 | 102.4 | 12 |
| 104 | HIndercaly Fen | B | 8.40 | 4.05 | 15.01 | 3.210 | 38.7 | 12 |  |  |  |  |  |  |

# TEMPORAL PATTERNS

## Mean Temporal Patterns of NH3

The seasonal variations in NH3 across all sites in the network are summarised in Figure 12, which shows the monthly mean of all site measurements, together with the minimum and maximum values monitored for each month. Monthly mean concentrations of all sites in 2007 were in the range 1.1 – 3.7 g NH3 m-3, whilst individual monitored monthly concentrations were in the range 0 – 22 g NH3 m-3.

The annual temporal profiles across all sites are also plotted for NH4+ to show the major patterns of concentrations (Figure 13). As with NH3, the monthly mean of all site measurements, together with the minimum and maximum values monitored for each month are shown. The monthly concentrations of individual sites were in the range 0.03 – 6.0 g NH4+ m-3, with monthly concentrations of all sites averaging between 0.39 – 1.4 g NH4+ m-3. Ammonium aerosol concentrations appeared to be much higher in 2003, which coincided with a very warm, dry spring that year. The higher concentration is also supported by elevated levels of aerosol NO3- and SO42- over the same period, monitored in the HNO3 monitoring network (Tang et al. 2007).

Figure 12: Mean monitored monthly NH3 concentrations from all sites in the network. The bars show the minimum and maximum concentrations for each month. The graphs are all plotted on the same scale, to allow a comparison of annual differences in concentrations to be made.

## Mean Temporal Patterns of aerosol NH4+

Figure 13: Mean monthly aerosol NH4+ concentrations from all sites in the network. The bars show the minimum and maximum concentrations monitored for each month.

## Comparison by dominant emission sources

The distribution of NH3 emissions for the UK is modelled by the AENEID model described by Dragosits et al. (1998) and currently applied in the NAEI. For agricultural emissions, parish statistics on livestock numbers and crop areas are combined with satellite-based land cover data to model emissions at a 1 km resolution, which are subsequently aggregated to the 5 km level. The resulting maps of dominant NH3 source sectors are shown in

Figure 14, for 1988 (no data for NI in this first emission map), 2003 (Dragosits 2005) and for 2005 (Dragosits 2007), for comparative purposes. Maps from 2000, 2001, 2002 and 2004 are also available, but not shown here. It is clear that there are significant regional patterns in the major contributing source sectors, and that there are very little changes in the map since 1988. However, there are visibly fewer grid squares for sheep emission in 2005, than previously, whilst the number of grid squares with emissions from crops & cut grass has increased.

Using the UK AENEID model, each site in the network is classified according to one of seven different dominant emission source categories (cattle, pig & poultry, sheep, fertilizer/crops, non-agricultural, non dominant, background, Table 4).

a) 1988			     	b) 2003				c) 2005

Figure 14: Classification of 5 km grid squares in UK according to estimated dominant source sector for NH3 emissions. Squares with emissions < 1 kg N ha-1 yr-1 are referred to as background. Squares with >45% from a given category are referred to as dominated by that source.  a) 1988 map for GB only, b) 2003 map for UK, c) 2005 map for UK.

Table 4: Classification of NAMN sites according to dominant emission source categories for the 5 km grid square containing site.

| No | Name | Map Ref | DOM_SOURCE 1988 | DOM_SOURCE 2003 | DOM_SOURCE 2005 |
| --- | --- | --- | --- | --- | --- |
| 1 | Bush OTC | nt243642 | Non-agricultural | Non-agricultural | Mixed* |
| 2 | Bush Cabin | nt247638 | Non-agricultural | Non-agricultural | Mixed* |
| 3 | Inverpolly | nc187088 | Background | Background | Background |
| 3B | Inverpolly 2 (met enc.) | nc187089 | Background | Background | Background |
| 4 | Penallt | so523095 | Cattle | Pigs & Poultry* | Mixed* |
| 5 | Priddy | st525526 | Cattle | Cattle | Cattle |
| 6 | Holme Lacy | so554357 | Cattle | Cattle | Cattle |
| 6B | Rosemaund | so564476 | Cattle | Cattle | Cattle |
| 7 | Glenshee | no117693 | Background | Mixed* | Mixed* |
| 7B | Gulabin Lodge | no110701 | Background | Background | Background |
| 8 | Stackpole | sr982947 | Mixed | Cattle* | Cattle* |
| 8B | Orielton | sr954992 | Cattle | Cattle | Cattle |
| 8C | Narberth | sn146127 | Cattle | Cattle | Cattle |
| 9 | Brown Moss NR | sj559396 | Cattle | Cattle | Cattle |
| 9B | Brown Moss NR 2 | sj563390 | Cattle | Cattle | Cattle |
| 10 | Bure Marshes | tg334161 | Mixed | Mixed | Mixed |
| 11 | Mere Sands Wood | sd447157 | Mixed | Pigs & Poultry* | Pigs & Poultry |
| 12 | Halladale | nc902488 | Background | Background | Background |
| 13 | Aston Rowant | su727979 | Mixed | Non-agricultural* | Non-agricultural |
| 14 | Ellon Ythan | nj945304 | Cattle | Mixed* | Mixed |
| 15 | Llynclys Common | sj273237 | Cattle | Cattle | Cattle |
| 16 | Northallerton | se360930 | Mixed | Cattle* | Mixed* |
| 17 | Easingwold | se540675 | Mixed | Pigs & Poultry* | Pigs & Poultry |
| 18 | Auchencorth Moss | nt221562 | Cattle | Mixed* | Mixed |
| 19 | Shetland | hu500400 | Background | Non-agricultural* | Non-agricultural |
| 20 | Drayton | sp162551 | Pigs & poultry | Mixed* | Mixed |
| 21 | Glensaugh | no664799 | Cattle | Cattle | Mixed* |
| 22 | Moor House | ny751334 | Background | Background | Background |
| 23 | North Wyke | sx659983 | Cattle | Cattle | Cattle |
| 24 | Rothamsted | tl123129 | Non-agricultural | Non-agricultural | Non-agricultural |
| 25 | Sourhope | nt867218 | Sheep | Mixed* | Mixed |
| 26 | Wytham Woods | sp452083 | Mixed | Non-agricultural* | Non-agricultural |
| 27 | Alice Holt | su809379 | Mixed | Pigs & Poultry* | Pigs & Poultry |
| 28 | Porton Down | su253365 | Mixed | Mixed | Mixed |
| 29 | Llydaw | sh695572 | Sheep | Mixed* | Mixed |
| 30 | Strathvaich Dam | nh348750 | Background | Background | Background |
| 31 | Eskdalemuir | nt235030 | Cattle | Non-agricultural* | Non-agricultural |
| 32 | High Muffles | se776939 | Cattle | Pigs & Poultry* | Mixed* |
| 33 | Stoke Ferry | tl700988 | Pigs & poultry | Non-agricultural* | Non-agricultural |
| 34 | Yarner Wood | sx789788 | Cattle | Cattle | Cattle |
| 35 | Lullington Heath | tq538016 | Cattle | Cattle | Mixed* |
| 36 | London, Bloomsbury | tq264789 | Non-agricultural | Non-agricultural | Non-agricultural |
| 36b | London, Victoria | tq291790 | Non-agricultural | Non-agricultural | Non-agricultural |
| 36C | London, Cromwell Rd | tq266791 | Non-agricultural | Non-agricultural | Non-agricultural |
| 37 | 5 Acres | sw794486 | Cattle | Cattle | Cattle |

Table 4 cont.: Classification of NAMN sites according to dominant emission source categories for the 5 km grid square containing site.

| No | Name | Map Ref | DOM_SOURCE 1988 | DOM_SOURCE 2003 | DOM_SOURCE 2005 |
| --- | --- | --- | --- | --- | --- |
| 38 | Sheffield | sk332870 | Non-agricultural | Non-agricultural | Non-agricultural |
| 38B | Sheffield 2 | sk339873 | Non-agricultural | Non-agricultural | Non-agricultural |
| 39 | Silsoe | tl088356 | Mixed | mixed | mixed |
| 40 | Sutton Bonington | sk505268 | Mixed | Cattle* | Cattle* |
| 41 | Lagganlia | nh856037 | Background | Background | Background |
| 42 | Castle Cary | st609319 | Cattle | Cattle | Cattle |
| 43 | Tadcaster | se452455 | Mixed | Mixed | Mixed |
| 44 | Hillsborough | ij243577 | Cattle | Mixed* | Cattle* |
| 45 | Lough Navar | ih065545 | Background | Cattle* | Cattle |
| 46 | Sibton | tm363722 | Mixed | Mixed | Mixed |
| 47 | Rum | nm408992 | Background | Non-agricultural* | Background* |
| 48 | Wem Moss | sj473343 | Cattle | Pigs & Poultry* | Cattle* |
| 49 | Frodsam | sj525795 | Pigs & poultry | Mixed* | Mixed |
| 50 | Swettenham Meadows | sj804674 | Cattle | Cattle | Cattle |
| 51 | Wybunbury Moss | sj698502 | Cattle | Cattle | Cattle |
| 52A | Fenn's Moss 1 | sj490365 | Cattle | Cattle | Cattle |
| 52B | Fenn's Moss 2 | sj478368 | Cattle | Cattle | Cattle |
| 52C | Fenn's Moss 3 | sj498378 | Cattle | Cattle | Cattle |
| 53 | Little Budworth | sj584658 | Mixed | Cattle | Cattle |
| 54 | Bickerton HIll | sj498527 | Cattle | Cattle | Cattle |
| 55 | Ruabon | sj225489 | Non-agricultural | Cattle* | Cattle |
| 56 | Wardlow Hay Cop | sk177737 | Cattle | Cattle | Cattle |
| 57 | Stanford | tl858948 | Pigs & poultry | Pigs & Poultry | Pigs & Poultry |
| 57B | Stanford 2 | TL836929 | Pigs & poultry | Pigs & poultry | Pigs & poultry |
| 58 | Redgrave + Lopham | tm050797 | Mixed | Pigs & Poultry* | Pigs & Poultry |
| 59 | Dunwich Heath | tm470680 | Mixed | Background* | Pigs & Poultry* |
| 60 | Edinburgh | nt253734 | Non-agricultural | Non-agricultural | Non-agricultural |
| 60B | Edinburgh 2 | nt263726 | Non-agricultural | Non-agricultural | Non-agricultural |
| 61 | Much Hoole | sd473231 | Pigs & poultry | Pigs & Poultry | Pigs & Poultry |
| 62 | Midge Hall | sd508231 | Mixed | Mixed | Mixed |
| 63 | Cardigan | sn185453 | Cattle | Cattle | Cattle |
| 64 | Pwllpeiran | sn798771 | Sheep | Mixed* | Mixed* |
| 65 | Allt a Mharcaidh | nh895024 | Background | Background | Background |
| 65 | Allt a Mharcaidh | nh895024 | Background | Background | Background |
| 66 | Dennington | tm276669 | Pigs & poultry | Pigs & Poultry | Pigs & Poultry |
| 67 | Fressingfield | tm261759 | Pigs & poultry | Pigs & Poultry | Pigs & Poultry |
| 68 | Bedlingfield | tm173684 | Pigs & poultry | Pigs & Poultry | Pigs & Poultry |
| 70 | Cwmystwyth | sn771742 | Sheep | Mixed | Mixed* |
| 71 | Myerscough | sd498399 | Cattle | Cattle | Cattle |
| 72 | Cardoun Burn | nx546658 | Background | Non-agricultural* | Mixed* |
| 73 | Jenny Hurn | sk816986 | Mixed | Mixed | Mixed |
| 73B | Marton | sk844819 | Mixed | Mixed | Mixed |
| 74 | Carlisle | ny468554 | Cattle | Cattle | Cattle |
| 75 | Westhay Moor | st455440 | Cattle | Cattle | Cattle |
| 76 | Pointon | tf128313 | Fertiliser/crops | Fertiliser/crops | Fertiliser/crops |
| 76B | Pointon 2 | tf128313 | Fertiliser/crops | Fertiliser/crops | Fertiliser/crops |
| 76C | Pointon 3 | tf128313 | Fertiliser/crops | Fertiliser/crops | Fertiliser/crops |

Table 4 cont.: Classification of NAMN sites according to dominant emission source categories for the 5 km grid square containing site.

| No | Name | Map Ref | DOM_SOURCE 1988 | DOM_SOURCE 2003 | DOM_SOURCE 2005 |
| --- | --- | --- | --- | --- | --- |
| 77 | Carradale | nr798378 | Cattle | Non-agricultural* | Non-agricultural |
| 78 | Auchincruive | ns379234 | Cattle | Cattle | Cattle |
| 78B | Auchincruive 2 | ns384229 | Cattle | Cattle | Cattle |
| 78C | Auchincruive 3 | ns379234 | Cattle | Cattle | Cattle |
| 79 | Coleraine | iC884211 | Cattle | Cattle | Cattle |
| 80 | Lyulphs Tower | ny403202 | Cattle | Cattle | Cattle |
| 81 | Pitmedden | nj883278 | Pigs & poultry | Pigs & Poultry | Pigs & Poultry |
| 82 | Brompton | se389988 | Mixed | Cattle* | Cattle |
| 83 | Barcombe Mills | tq438149 | Cattle | Cattle | Cattle |
| 84 | Thursley Common | su910404 | Mixed | Pigs & Poultry* | Mixed* |
| 85 | Savarnake | su055888 | Cattle | Cattle | Cattle |
| 86 | Lakes | sd337941 | Cattle | Cattle | Cattle |
| 87 | Thetford | tl944841 | Mixed | Pigs & Poultry* | Pigs & Poultry |
| 88 | Sherwood | sk163905 | Background | Cattle* | Cattle |
| 89 | Rannoch | nn603533 | Background | Background | Background |
| 90 | Coalburn | ny693782 | Non-agricultural | Mixed* | Mixed |
| 91 | Tummel | nn744611 | Non-agricultural | Mixed* | Mixed |
| 92 | Loch Awe | nm966115 | Cattle | Background* | Background |
| 93 | Llynn Brianne | sn816484 | Mixed | Sheep* | Mixed* |
| 94 | Alice Holt (2) | su805427 | Non-agricultural | Mixed | Mixed |
| 95 | Glenshee Hotel | no111699 | Background | Mixed* | Mixed |
| 95B | Glenshee Hotel | no110701 | Background | Background | Background |
| 96 | Oldmeldrum | NJ832273 | Pigs & Poultry | Pigs & Poultry | Mixed* |
| 97 | Detling | TQ801597 | Mixed | Mixed | Mixed |
| 98 | Harwell | su474863 | Pigs & Poultry | Mixed* | Non-agricultural* |
| 99 | Ladybower | SK164892 | Mixed | Mixed | Mixed |
| 100 | Plas Y Brenin | SH716578 | Sheep | Mixed | Mixed |
| 102 | Caenby | SK993900 | Mixed | Pigs & Poultry | Mixed* |
| 103 | Goonhilly | SW723214 | Cattle | Cattle | Cattle |

* where site classification has changed.

In Figure 15, the average seasonal cycles in NH3 and NH4+ concentration of grouped sites from four different emission source categories are compared. There are a number of broad patterns in the temporal trends that is related to emission source types.

Background sites (NH3 emission < 1 kg N ha-1 yr-1): Clear summer maximum with minimum concentrations occurring in winter. The summer peak is probably related to increased land surface ammonia emissions in warm, dry summer conditions, both from low density grazing livestock and from vegetation compensation point.

Sheep: Similar to that for background, although the summer maximum in NH3 emission is larger than background sites, because grazing emissions is larger.  It is notable the peak NH3 concentration occurs later for background areas (July-September) than sheep areas (June-August).  This may be related to the seasonal presence of lambs, which are only present for the first part of the summer.

Cattle / Pig & poultry: In areas with intensive livestock farming, concentrations are largest in spring and autumn, corresponding to periods of manure application to land. For cattle areas, the peaks occur in March and September, while in pig/poultry areas, the autumn peak is larger than the spring peak, since this is the main period for manure application in arable areas (before sowing of autumn crops). Ammonia concentrations in these areas are also larger in summer than winter, due to warmer conditions promoting volatilizations, adding to the complex temporal profile.

Figure 15: Temporal trends in NH3 concentrations from the mean data (1996-2007) of sites in the NAMN classified as dominated by different emission categories: cattle, sheep, pig & poultry and background (based on 1988 emissions classification).

For NH4+ aerosol, there is less relationship to the dominant ammonia source sectors in the data since this is a regional product (Figure 16). The network results provide a comprehensive account of the seasonal variability of NH3 and NH4+ for different regional areas across the UK. It is clear that the NH3 seasonal patterns vary greatly between sites, which depends on regional source type (e.g. sheep, cattle, pigs etc.), while for NH4+ aerosol, there is a significant correlation in inter-annual variability between sites, due to synoptic meteorology and variation with long range transboundary pollutant transport.

Figure 16: Temporal trends in aerosol NH4+ concentrations from the mean data (1996-2007) of sites in the NAMN classified as dominated by different emission categories: cattle, sheep, pig & poultry and background.

# SPATIAL PATTERNS

National maps of both gaseous NH3 and aerosol NH4+ concentrations are derived from the NAMN. Data from the network confirmed the high spatial variability in NH3 concentration (0.05-15 g m-3) (Figure 17), reflecting the large regional variability in NH3 emissions (Sutton et al. 2001a). Aerosol NH4+ on the other hand, shows a spatially smooth concentration field (Figure 17), as predicted.

2007 Annual NH3 Concentration Map 		FRAME V6.12 (2005)	        Monitored points overlain onto FRAME

2007 Annual NH4+ Concentration Map		FRAME V6.12 (2005)	        Monitored points overlain onto FRAME

Figure 17: Interpolated atmospheric NH3 and aerosol NH4+ concentration maps for 2007 from the UK NAMN at 10 km x 10 km grid resolution, and compared with FRAME V6.12 (2005) (Dore 2006). NH3 concentrations at ground level are highly spatially variable. As a secondary product, NH4+ aerosol has a much smoother spatial distribution than NH3.

There are clear regional patterns in the mapped concentration fields for NH3, which reflects emission source types/strengths across the country. Some general pattern in NH3 concentration can be picked out. A broad pattern of small air concentrations occur in the NW Scottish Highlands of less than 0.2 µg m-3. Low concentrations also occur in S / SE England and Cornwall of less than 1 µg m-3. NH3 concentrations do not appear to show much variation across central southern England.

The largest ammonia concentrations were seen in source areas, particularly in areas with intensive cattle, pig and poultry farming, e.g. East Anglia.  Even at a regional level, variability in NH3 concentrations is apparent, since smaller concentrations are monitored in areas with few ammonia sources within only a few tens of kilometres. For example, at North Wyke in Devon (site 23), the 2007 annual mean concentration was 2.1 µg m-3, while 25 km southeast, the concentration at Yarner wood (site 34) was 0.56 µg m-3.

The CEH AENEID model of spatial NH3 emissions, as used in the National Atmospheric Emissions Inventory (NAEI) provides input to the FRAME model for comparison with the NAMN results. Figure 17 shows the modelled concentration fields for NH3 and NH4+ from the FRAME model, using 2005 emission data as input (Dore et al. 2006). While the overall comparison is good, the measurements are slightly larger than FRAME in remote areas, and less than FRAME in source areas.

The high spatial variability is also seen in the two selected meso-scale variability study areas in East Anglia and around the Shropshire/Welsh border. The measurements on the Norfolk to Suffolk transect cover both intensive farming sources and nearby sink areas and gave mean concentrations in the range of 0.86 (Dunwich Heath, S59) to 7.9 µg NH3 m-3 (Bedingfield, S68), with substantial local gradients.

Figure 18: Map of East Anglia showing (as coloured points) the gradient in NH3 concentrations determined by the monitoring network on a background of the FRAME 2005 (V6.12) estimates.

By contrast, particulate NH4+ is a slowly formed secondary product with a longer residence time in the atmosphere and is expected to show less spatial variation. For the 2007 map (Figure 17), the concentrations ranged from 1.5 µg m-3 in central London (S36C) and 1.3 µg m-3 in a high SO2 emission area (Sutton Bonington S40) to a low concentration of 0.25 µg m-3 at Rum (S47) on the northwest coast of Scotland. Concentrations at adjacent sites were also very similar. For example, the mean monitored NH4+ concentration in 2007 at North Wyke (S23) and Yarner Wood (S34) were 0.75 and 0.93 µg m-3, respectively. Initially, NH4+ aerosol was sampled at all 57 DELTA sites to demonstrate the predicted smooth concentration field, since adjacent sites should have similar concentrations. Following a review in November 2000 to reduce the number of aerosol sampling sites, and other changes in the course of running the network (e.g. expansion of HNO3 network), there are currently 46 sites providing NH4+ aerosol measurements.

## Local Variability

It is recognised that mapping of NH3 concentration and deposition at a national scale using monitoring and atmospheric transport models needs to consider the extent of sub-grid variability and the representativity of sampling points. In the UK NAMN, NH3 concentrations are compared with estimates from an emission inventory and atmospheric transport model at 5 km grid resolution. Substantial variability in NH3 concentration and deposition is expected even at the sub-5 km level (Dragosits et al. 2002). Therefore, spatially detailed local scale NH3 monitoring has been carried out, and compared with the national inventory and a local-scale dispersion model (LADD; Theobald et al. 2004) at a sub-1 km level to assess the extent to which the monitoring location is representative (Tang et al. 2001a, Sutton et al. 2004).

- Glenshee: Spatially detailed NH3 monitoring was made across an upland 5 km grid square containing the Glenshee network site (S7, emission source sector = cattle) (Tang et al. 2001a).

- East Anglia and Cheshire/Shropshire, linked to the LANAS (Landscape Analysis of Nitrogen and Abatement Strategies) project of the NERC GANE programme (Theobald et al. 2004).

The analysis showed that a significant amount of variation comes from landscape (sub 5 km) level variations that cannot be easily treated in either national 5 km or European 50 km modelling. Sites with a major effect on the interpolated air concentration field are those which either a) show a large concentration in a clean region or b) show a small concentration in a polluted region. The measurements have also served to provide an important test of the 5 km scale atmospheric modelling of NH3 using FRAME, and results from these two studies have also been fully assessed through the use of local scale atmospheric transport models, the LADD model (Theobald et al. 2004).

In 2007, another local scale (sub-5 km) variability assessment of ammonia, in conjunction with NitroEurope Landscape Analysis has also been in progress at a UK study landscape. The chosen study landscape is a 6 km x 6 km area in Southern Scotland, with emissions from poultry farms, sheep and cattle grazing, and some horses in close proximity to semi-natural areas (heathlands and forests). For reasons of confidentiality, the identity and location of the study landscape cannot at this time be disclosed. A total of 30 passive sampling sites (using the CEH ALPHA samplers) were established within the 36 km2 grid area in mid-September 2006, and two intensive monitoring periods (monthly) were carried out from October to November 2006 to provide an initial assessment. Continuous measurement of monthly atmospheric NH3 concentrations was then started in April 2007, and will run for 2 years. Results from the first year of measurements are summarised in Figure 19.

Under UK NAMN, the objective of the local variability study is to provide additional information that is important for assessing representativity of existing monitoring sites and the spatial variability in local NH3 impacts on semi-natural ecosystems. This follows on from previous sub-grid variability studies made at the Glenshee upland site and subsequently in East Anglia and Cheshire/Shropshire.

Under NitroEurope (http://www.nitroeurope.eu/), the wider remit is to assess how N management can modify reactive nitrogen (Nr) fluxes at local and landscape scales, with particular emphasis on Nr interactions with GHG fluxes. The project is carried out over six European study landscapes (Italy, Poland, France, The Netherlands, Denmark, and the UK). A PhD studentship appointed under NitroEurope is contributing to this assessment for the Scottish landscape. NitroEurope is therefore providing additional resources which are of added value and benefits for the UK NAMN.

Figure 19: Monitored annual mean NH3 concentrations (Apr07-Mar08) at the 30 sampling locations within the Southern Scottish study landscape (Vogt 2008)

# Trends in ammonia concentrations

Trends in atmospheric NH3 are not easily detectable at individual sites due to significant inter-annual variability that are linked to meteorological differences and periodic local influences. Therefore, a trend assessment was based on results from multiple sites. In Figure 20-21 and Figure 23-24, the long-term trend in mean monitored and seasonally-detrended mean NH3 concentrations of sites grouped into four different emission source sectors are compared (sites are classified according to 1988 NH3 emission sector data/map). The seasonal detrending was derived from the mean seasonal cycle for the whole period normalized to 1, and then multiplying each monthly value by the appropriate value.

## Emission sector: Background

For analysis, background sites were grouped according to the implemented methodology, delta and passive. This is to ensure consistency and continuity in the sampling methods for the analysis of trends. Figure 20a (LHS) are selected from 8 background sites that used the DELTA method over the entire period (S3 Inverpolly, S7B Gulabin Lodge (replaced by S95 Glenshee Lodge from Jul06), S12 Halladale, S19 Shetland, S22 Moor house, S30 Strahvaich Dam, S41 Lagganlia, S45 Lough Navar and S47 Rum), whereas the mean data of 8 passive sampling sites were used in Figure 20a (RHS) (S3 Inverpolly, S22 Moorhouse, S41 Lagganlia, S65 Allt a Mharcaidh, S88 Sherwood, S89 Rannoch, S92 Loch Awe, S95 Glenshee)

From the graphs, ammonia concentrations appeared to be lower at sites where measurements were made with passive samplers, compared with background sites with delta measurements. However, the reason for the higher values at background delta sites is due to the unexpectedly high summer concentrations at Halladale (S12). The temporal patterns are clearly reproducible between years, with monitored mean monthly concentrations in the range of 0.06 – 1.6 µg NH3 m-3 (0.0 – 0.81 µg NH3 m-3, excluding S12 data). There appears to be an upward trend in NH3 concentrations. However, the trend is not statistically significant in the seasonally de-trended values, which is derived by dividing the concentrations by the national average seasonal cycle. The apparent increase may be a feature of the reduction in SO2 emissions over the same period, leading to a longer atmospheric lifetime of NH3, thereby increasing NH3 concentrations in remote areas.

Figure 20: (a) Top graphs: Long-term trend in mean monitored (--o--) and seasonally-detrended mean NH3 concentration (__(__ )  from background sites (defined by 5 km grid average emissions <1 kg N ha-1 yr-1) in the NAMN. LHS: data from 8 sites where measurements were made using the DELTA system throughout, RHS: data from 8 sites where all measurements are made using the Diffusion Tube (Sep96 – Apr00) and subsequently the ALPHA sampler (from May00). Sites with less than 2 years data were excluded from this analysis.  (b) Bottom graphs: Inter-annual variability in NH3 concentrations.

## Emission sector: Cattle

Figure 21: (a) Top graphs: Long-term trend in mean monitored (--o--) and seasonally-detrended mean NH3 concentration (__(__ )  from sites in grid squares dominated by emissions from cattle in the NAMN. LHS: data from 19 sites where measurements are made using the DELTA system throughout, RHS: data from 18 sites where all measurements are made using the Diffusion Tube (Sep96 – Apr00) and subsequently the ALPHA sampler (from May00). Sites with less than 2 years data were excluded from this analysis.  (b) Bottom graphs: Inter-annual variability in NH3 concentrations.

In cattle dominated areas, there is a slight (non-significant) increase in NH3 concentrations (Figure 21), although emission from this sector across the UK has not changed much since 2002 (Figure 22). For the purpose of consistency in monitoring methods for analysing long-term trends, data in Figure 21a (LHS) are selected from 19 cattle sites that used the DELTA method over the entire period, whereas the mean data of 18 passive sampling sites were used in Figure 21a (RHS) . In both graphs, the temporal patterns are clearly reproducible between years, with monitored mean monthly concentrations in the range of 0.9 – 4.5 µg NH3 m-3.

Figure 22: Time series of NH3 Emissions (ktonnes). Reproduced from Dore et al. 2007.

## Emission sector: Pig & Poultry

Figure 23: (a) Top graphs: Long-term trend in mean monitored (--o--) and seasonally-detrended mean NH3 concentration (__(__ )  from sites in grid squares dominated by emissions from sheep in the NAMN. Bottom graphs: Inter-annual variability in NH3 concentrations. LHS: data from 5 sites where measurements are made using the DELTA system throughout, RHS: data from 11 sites where all measurements are made using the Diffusion Tube (Sep96 – Apr00) and subsequently the ALPHA sampler (from May00). Since the passive methods are subject to a correction derived from their regression against the DELTA system, caution needs to be exercised in interpreting long-term trends where the sampling methodologies are changed (from Diff. Tube to ALPHA in May 2000). (b) Bottom graphs: Inter-annual variability in NH3 concentrations.

There is some indication that NH3 concentrations have decreased in pig/poultry areas (Figure 23), which is consistent (but not as large as) with the estimated reduction in NH3 emissions from these sectors. Again, for the purpose of consistency in monitoring methods for analysing long-term trends, data in Figure 23a (LHS) are selected from 2 pig & poultry sites (S20 Drayton, S33 Stoke Ferry) that used the DELTA method over the entire period, whereas the mean data of 10 passive sampling sites were used in Figure 23a (RHS). In both graphs, the temporal patterns are clearly reproducible between years, with monitored mean monthly concentrations in the range of 0.74 – 8.4 µg NH3 m-3. The larger NH3 concentrations at passive sites are due to the deployment of passive samplers in source regions to explore regional and local scale variability.

## Emission sector: Sheep

There are 5 sites in the UK NAMN that are classed as being in sheep emission grid squares (S25 Sourhope, S29 Llydaw, S64 Pwllpeiran, S70 Cwmystwyth, S100 Plas Y Brenin). Overall there is a slight upward trend in NH3 concentrations (non-significant) (Figure 24). There is however a degree of uncertainty in the disaggregation of emission data for sheep, and subsequent classification of 5 km grid squares in the AENEID emission model, particularly in Wales. Using classification from the 2003 emission source category map, only 3 sites were classed as sheep, with S70 Cwmystwyth being the only site not to have changed status. The other 2 sites are S93 Llynne Brianne and S99 Ladybower. Under the latest 2005 emission category map, S99 Ladybower is the only site remaining in this category.

Figure 24: LHS: Long term trend in mean monitored (--o--) and seasonally-detrended mean NH3 concentration (__(__ )  from 2 sites in grid squares dominated by emissions from sheep in the NAMN. Measurements at Sourhope, Cwmystwyth, Plas Y Brenin were made using the DELTA system throughout, whilst passive samplers were used at Llydaw and Pwllpeiran. RHS: Inter-annual variability in NH3 concentrations.

# trends in aerosol ammonium concentrations

For NH4+ aerosol, it has already been shown that this is regional product, and there is therefore less relationship to the dominant ammonia source sectors in the data. This is confirmed by very similar long-term trends in mean monitored and seasonally-detrended NH4+ concentrations derived for sites grouped into different emission source sectors (data not shown). Analysis was therefore made using all measurement site data (Figure 25). The overall dataset shows no detectable trend in NH4+ concentrations, indicating that a longer measurement period is needed before trends can be detected.

Figure 25: LHS: Long-term trend in mean monitored (--o--) and seasonally-detrended mean NH4+ aerosol concentration (__(__ )  from all sites in the UK NAMN. The seasonal detrending was derived from the mean seasonal cycle for the whole period normalized to 1, and then multiplying each monthly value by the appropriate value. RHS: Inter-annual variability in NH3 concentrations.

## Estimation of UK ammonia dry deposition

UK budgets of NH3 dry deposition is estimated using the CBED (Concentration Based Estimates of Deposition) inferential model of Smith et al. (2000) as applied by NEGTAP (2001). The model combines estimates of NH3 air concentration with a resistance analysis applying canopy resistances for forest and moorland vegetation, and the canopy compensation point model (e.g. Sutton et al. 1995; Nemitz et al. 2004) for exchange over grassland and croplands. This ‘inferential approach’ can use air concentration estimates from either models or measurements.

The regression between NH3 measurements and FRAME is used to scale the FRAME estimates to the network, and the transformed FRAME estimates are then applied as input to the inferential model. This approach is considered to provide the best estimate of the UK concentration field overall. The outputs of this model are maps of NH3 dry deposition to the major land-cover types, forest, moorland (and semi-natural vegetation), agricultural grassland, arable, and urban. To estimate the budget of UK NH3 dry deposition, these maps are combined according to percentage of land cover occurrence in each 5 km grid square, which gives a map of grid average NH3 dry deposition. The deposition models are also applied to estimate dry deposition of aerosol NH4+ in the UK which gives an estimate of the effect of new data on total dry deposition budgets and NH3 and NH4+ exports from the UK (Table 5) estimated under the Defra Acid Deposition Processes project. There has been little change in the modelled deposition of both oxidised and reduced nitrogen to the UK. Generally speaking, the above changes in UK budgets are well within the expected variability (or uncertainty) we obtain with these models.

Table 5:  Estimated annual budgets of UK nitrogen deposition for the period 1997-2006 (kt year-1)

|  |  | 1997 | 1998 | 1999 | 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| NOy | wet+cloud | 102 | 98 | 103 | 98 | 105 | 107 | 77 | 99 | 104 | 94 |
|  | dry (NOx) | 37 | 33 | 31 | 32 | 28 | 22 | 25 | 17 | 19 | 17 |
|  | dry (NOy) |  |  |  | 89 | 101 | 84 | 111 | 73 | 82 | 78 |
|  | aerosol |  |  |  | 7 | 9 | 9 | 13 | 9 | 9 | 8 |
|  | total |  |  |  | 194 | 215 | 199 | 201 | 181 | 195 | 180 |
| NHx | wet+cloud | 116 | 121 | 121 | 104 | 120 | 118 | 87 | 112 | 121 | 135 |
|  | dry | 62 | 53 | 50 | 43 | 52 | 51 | 58 | 49 | 54 | 53 |
|  | aerosol |  |  |  | 9 | 12 | 11 | 15 | 10 | 10 | 10 |
|  | total |  |  |  | 156 | 184 | 180 | 160 | 172 | 185 | 197 |

The current best estimate of NH3 dry deposition for 2006 provided by the transformed FRAME approach is 53 kt (N) yr-1 for the UK. Overall, reduced nitrogen deposition contributes on average 47% of the UK deposited nitrogen, while oxidized nitrogen contributes 53%. This shows the regional scale of the fluxes.  NH3 dry deposition is a major term in the UK N deposition budget (~53 kT-N), contributing on average 14 % of the UK deposited nitrogen. Since NH3 also deposits preferentially to semi-natural ecosystems, for the deposition received by these habitats, by far the largest fraction is deposited as reduced nitrogen.

The model may also be used to provide inputs to sensitive ecosystem types (receptor basis), as used in the APIS website (http://www.apis.ceh.ac.uk) which provides a searchable database and information on pollutants and their impacts on habitats and species. The modelling demonstrates that ammonia is one of the largest atmospheric nitrogen inputs to sensitive ecosystems over many parts of the UK.

# ACKNOWLEGEMENTS

This work was carried out with funding from the Department for Environment, Food and Rural Affairs (DEFRA), and from supporting CEH programmes. The assistance of the network of site operators, and CEH colleagues is also gratefully acknowledged.

# REFERENCES

Dore, C.J. JD Watterson, TP Murrels, NR Passant, MM Hobson, SL Choudrie, G Thistlethwaite, A Wagner, J Jackson, Y Li, T Bush, KR King, J Norris, PJ Coleman, C Walker, RA Stewart, JWL Goodwin, I Tsagatakis, C Conolly, MK Downes, N Brophy & MR Hann. UK Emissions of Air Pollutants 1970 to 2005. AEA Energy & Environment Report 30/11/2007 (http://www.naei.org.uk/reports.php).

Dore A.J., Vieno M., Tang Y.S., Dragosits U., Dosio A., Weston K.J. & Sutton M.A. (2006). Modelling the atmospheric transport and deposition of sulphur and nitrogen over the United Kingdom and assessment of the influence of SO2 emissions from international shipping. Atmospheric Environment 40(18), 3316-3326.

Dragosits U., Sutton M.A., Place C.J. and Bayley A. (1998) Modelling the spatial distribution of ammonia emissions in the United Kingdom. Environ. Pollut. (Nitrogen Conference Special Issue).

Dragosits U., Theobald M.R., Place C.J., Lord E., Webb J., Hill J., ApSimon H.M. and Sutton M.A. (2002) Ammonia, emission, deposition and impact assessment at a field scale: a case study of sub-grid spatial variability. Environmental Pollution 117 (1) 147-158.

Dragosits U. & Sutton M.A. (2005) Maps of Ammonia emissions from agriculture, waste, nature and other miscellaneous sources for the NAEI 2003. Report to AEAT / DEFRA.

Dragosits U. & Sutton M.A. (2007) Maps of Ammonia emissions from agriculture, waste, nature and other miscellaneous sources for the NAEI 2005. Interim report on the National Atmospheric Emission Inventory (NAEI) and Greenhouse Gas Inventory (GHGI) to AEAT for Defra.

Ferm, M. (1979) Method for determination of atmospheric ammonia. Atmos. Environ., 13, 1385-1393

Fournier, N., V.A. Pais, M.A. Sutton, K.J. Weston, U. Dragosits, S.Y. Tang & J. Aherne (2002). Parallelisation and application of a multi-layer atmospheric transport model to quantify dispersion and deposition of ammonia over the British Isles. Environmental Pollution, 116, 95-107.

NEGTAP (2001) Transboundary Air Pollution: Acidification, Eutrophication and Ground Level ozone in the UK. Report of the National Expert Group on Transboundary Air Pollution, DEFRA, London

Nemitz E., Sutton M.A., Wyers G.P. and Jongejan P.A.C. (2004): Gas-particle conversions above a Dutch heathland: I. Surface exchange fluxes of NH3, SO2, HNO3 and HCl. Atmos. Chem. Phys. 4, 989-1005.

Singles, R.J., M.A. Sutton & K.J. Weston (1998) A multi-layer model to describe the atmospheric transport and deposition of ammonia in Great Britain. Atmos. Env., 32, 393-399.

Smith R.I., Fowler D., Sutton M.A., Flechard C. and Coyle M. (2000) Regional estimation of pollutant gas deposition in the UK: model description, sensitivity analyses and outputs. Atmospheric Environment 34, 3757-3777.

Sutton, M.A., Place, C.J., Eager, M., Fowler, D. & Smith, R.I. (1995). Assessment of the magnitude of ammonia emissions in the United Kingdom. Atmospheric Environment 29(12), 1393-1411.

Sutton. M.A., Tang. Y.S., Miners. B. and Fowler. D. (2001a). A new diffusion denuder system for long-term, regional monitoring of atmospheric ammonia and ammonium. WASP: Focus, 1, 145-156.

Sutton M.A., Miners B., Tang Y.S., Milford C., Wyers G.P., Duyzer J.H. and Fowler D. (2001b) Comparison of low-cost measurement techniques for long-term monitoring of atmospheric ammonia. J. Env.  Monit.,  3, 446-453.

Sutton, M.A, Theobald, M, Dragosits U, Place C.J, Tang Y.S, Love L, Van Dijk N, Fowler D, Smith J, Sozanska M. Scholefield D. Jarvis S.C. Del Prado A. Brown L. Angus A. Hodge I. Webb J. Wade A. & Whitehead P. (2004) Landscape analysis of the transport, transformation and fate of reactive nitrogen and abatement strategies (LANAS): GANE NERC Final Report. Mar 2004, 7pp.

Tang, Y.S., Dragosits, U., Theobald, M.R. Fowler D. and Sutton M.A. (2001a) Sub-grid variability in ammonia concentrations and dry deposition in an upland landscape. In: Air surface exchange of gases and particles: Poster proceedings. (Eds. D. Fowler, C.E.R. Pitcairn, L. Douglas and J.W. Erisman) pp 48-57, CEH Edinburgh.

Tang, Y.S., Cape, J.N. and Sutton, M.A. (2001b). Development and types of passive samplers for NH3 and NOx. In Proceedings of the International Symposium on Passive Sampling of Gaseous Pollutants in Ecological Research. TheScientificWorld, 1, 513-529.

Tang Y.S. & Sutton M.A. (2003) Quality management in the UK national ammonia monitoring network.  In: Proceedings of the International Conference: QA/QC in the field of emission and air quality measurements: harmonization, standardization and accreditation, held in Prague, 21-23 May 2003 (eds. Borowiak A., Hafkenscheid T., Saunders A. and Woods P.) pp297-307.  European Commission, Ispra, Italy.

Tang Y.S, M.A. Sutton, I. Simmons, L. Love, E.Vogt, N. van Dijk, J.N. Cape, R. I. Smith, E. Armas-Sanchez, H. Lawrence & G. Hayman (2007) Monitoring of nitric acid, particulate nitrate and other species in the UK: Interim report under the UK Acid Deposition Monitoring Network to NETCEN/defra.

Theobald M, Dragosits U, Place C.J, Smith J.U, Brown L, Scholefield D, Webb J, Whitehead P.G, Angis A, Hodge I.D, Fowler D. & Sutton M.A. (2004)   Modelling nitrogen fluxes at the landscape scale. WASP: Focus, 4(6), 135-142.

Vogt E, Braban C, Dragosits U & Sutton M (2008). Assessing atmospheric ammonia dispersion at the landscape scale. Poster to be presented at IGAC 10th International Conference, Bridging the scales in Atmospheric Chemistry: Local to Global, 7 to 12 September 2008 in Annecy, France.

# APPENDIX

## Monthly ammonia data in the UK NAMN

Gaseous NH3 (µg NH3 m-3)

| Site | S1L | S 1R | S1 | S2 | S3B | S3B | S4 | S6B | S8B | S9B | S9B | S10 | S11 | S11 | S12 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Method | D | D | T | T | D | T | D | D | D | D | T | D | D | T | D |
| Jan | 1.05 | 0.98 | 0.96 | 0.59 | 0.02 | 0.04 | 0.64 | 1.51 | 0.88 | 2.30 | 2.21 | 0.82 | 2.50 | 2.18 | 0.21 |
| Feb | 1.93 | 1.88 | 1.77 | 1.00 | 0.03 | 0.02 | 0.61 | 10.54 | 5.58 | 4.48 | 3.94 | 0.63 | 1.70 | 1.82 | 0.26 |
| Mar | 1.46 | 1.43 | 1.30 | 0.59 | 0.06 | 0.07 | 8.56 | 2.37 | 2.63 | 3.85 | 3.67 | 1.31 | 3.19 | 3.51 | 0.28 |
| Apr | 2.42 | 2.13 | 2.22 | 1.40 | 0.17 | 0.16 | 4.25 | 5.87 | 1.31 | 9.10 | 5.35 | 2.13 | 0.08 7 | 2.55 | 0.71 |
| May | 1.25 | 1.22 | 1.28 | 0.76 | 0.05 | 0.04 | 1.63 | 3.32 | ND 9 | 2.56 | 1.80 | 2.06 | 1.53 | 1.06 | 0.42 |
| Jun | 1.24 | 1.38 | 1.27 | 0.58 | 0.11 | 0.08 | 1.21 | 3.05 | 1.28 | 2.70 | ND 9 | 1.09 | 1.24 | 1.15 | 1.09 |
| Jul | 1.35 | 1.39 | 1.50 | 0.97 | 0.05 | 0.05 | 1.14 | 1.69 | 1.28 | 1.94 | 1.45 | 1.21 | 1.07 | 1.04 | 0.90 |
| Aug | 1.94 | 2.01 | 1.95 | 0.89 | 0.07 | 0.02 | 2.57 | 3.74 | 0.16 | 2.35 | 2.12 | 1.06 | 1.01 | 0.92 | 0.70 |
| Sep | 2.64 | 2.74 | 2.80 | 1.04 | 0.07 | 0.07 | 2.57 | 3.52 | 1.34 | 2.23 | 2.21 | 1.18 | 1.29 | 1.24 | 0.46 |
| Oct | 1.38 | 1.44 | 1.45 | 0.62 | 0.05 | 0.07 | 1.05 | 2.10 | 1.31 | 1.69 | 1.90 | 0.64 | 1.29 | 1.24 | 0.41 |
| Nov | 1.39 | 1.42 | 1.32 | 0.61 | 0.03 | 0.02 | 1.05 | 2.24 | 1.81 | 1.69 | 2.02 | 0.47 | 0.98 | 1.01 | -0.03 7 |
| Dec | 1.45 | 1.72 | 1.37 | 0.39 | 0.02 | 0.01 | 0.68 | 1.39 | 1.12 | 1.43 | 1.65 | 0.36 | 0.52 | 0.83 | 0.14 |
| Mean | 1.62 | 1.65 | 1.60 | 0.79 | 0.06 | 0.05 | 2.16 | 3.44 | 1.70 | 3.03 | 2.58 | 1.08 | 1.48 | 1.54 | 0.51 |
| Min | 1.05 | 0.98 | 0.96 | 0.39 | 0.02 | 0.01 | 0.61 | 1.39 | 0.16 | 1.43 | 1.45 | 0.36 | 0.52 | 0.83 | 0.14 |
| Max | 2.64 | 2.74 | 2.80 | 1.40 | 0.17 | 0.16 | 8.56 | 10.54 | 5.58 | 9.10 | 5.35 | 2.13 | 3.19 | 3.51 | 1.09 |
| SD | 0.498 | 0.480 | 0.510 | 0.281 | 0.042 | 0.043 | 2.280 | 2.558 | 1.417 | 2.109 | 1.214 | 0.565 | 0.755 | 0.819 | 0.304 |
| CV (%) | 30.6 | 29.1 | 31.9 | 35.7 | 71.2 | 77.5 | 105.4 | 74.3 | 83.4 | 69.6 | 47.1 | 52.4 | 50.9 | 53.0 | 59.9 |
| N | 12 | 12 | 12 | 12 | 12 | 12 | 12 | 12 | 11 | 12 | 11 | 12 | 11 | 12 | 11 |

| Site | S13 | S14 | S15 | S15 | S16 | S17 | S18L | S18R | S18 | S19 | S20 | S21 | S21 | S22 | S22 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Method | D | D | D | T | D | D | D | D | T | D | D | D | T | D | T |
| Jan | 0.53 | 1.99 | 0.86 | 0.69 | 1.44 | 0.10 | 0.48 | 0.41 | 0.41 | 0.09 | 0.75 | 0.15 | 0.12 | 0.37 | 0.39 |
| Feb | 0.48 | 1.64 | 1.70 | 1.54 | 1.90 | 1.56 | 1.48 | 1.32 | 1.49 | 0.09 | 0.96 | 0.24 | 0.17 | 0.35 | 0.25 |
| Mar | 3.58 | 2.26 | 1.31 | 1.51 | 2.32 | 0.56 | 0.66 | 0.51 | 0.57 | 0.15 | 1.29 | 0.31 | 0.21 | 0.51 | 0.37 |
| Apr | 5.45 | 2.57 | 3.63 | 3.53 | 5.97 | 5.40 | 1.20 | 0.95 | 1.27 | 0.16 | 4.87 | 0.67 | 0.52 | 0.92 | 0.70 |
| May | 2.62 | ND 8 | 1.50 | 1.38 | 5.43 | 1.38 | 0.55 | 0.48 | 0.57 | 0.16 | 3.00 | 0.34 | 0.27 | 0.46 | 0.39 |
| Jun | 10.18 | 5.05 | 1.55 | 1.38 | 3.24 | 1.09 | 0.77 | 0.72 | 0.73 | 0.17 | 1.75 | 0.33 | 0.22 | 0.40 | 0.37 |
| Jul | 1.27 | 7.77 | 1.11 | 1.00 | 6.09 | 0.72 | 0.58 | 0.49 | 0.64 | 0.13 | 1.44 | 0.20 | 0.16 | 0.59 | 0.29 |
| Aug | 1.79 | 6.19 | 1.47 | 1.34 | 5.48 | 0.79 | 0.75 | 0.63 | 0.70 | 0.15 | 1.66 | 0.37 | 0.30 | 0.34 | 0.50 |
| Sep | 2.38 | 4.79 | 1.68 | 1.55 | 5.80 | 1.23 | 0.55 | 0.45 | 0.57 | 0.00 7 | 2.51 | 0.37 | 0.29 | ND 8 | 0.57 |
| Oct | 0.67 | 14.14 | 1.74 | 1.46 | 4.74 | ND 8 | 1.06 | 1.01 | 1.05 | 0.21 | 1.21 | 0.40 | ND 9 | 0.30 | 0.19 |
| Nov | 0.62 | 9.01 | 1.53 | 1.32 | 3.02 | 2.51 | 0.51 | 0.45 | 0.46 | 0.04 | 0.84 | 0.20 | 0.11 | 0.25 | 0.30 |
| Dec | 0.29 | ND 8 | 0.92 | 0.80 | 2.42 | 1.34 | 0.79 | 0.74 | ND 11 | 0.06 | 0.66 | 0.20 | 0.10 | 0.16 | 0.09 |
| Mean | 2.49 | 5.54 | 1.58 | 1.46 | 3.99 | 1.52 | 0.78 | 0.68 | 0.77 | 0.13 | 1.75 | 0.31 | 0.22 | 0.42 | 0.37 |
| Min | 0.29 | 1.64 | 0.86 | 0.69 | 1.44 | 0.10 | 0.48 | 0.41 | 0.41 | 0.04 | 0.66 | 0.15 | 0.10 | 0.16 | 0.09 |
| Max | 10.18 | 14.14 | 3.63 | 3.53 | 6.09 | 5.40 | 1.48 | 1.32 | 1.49 | 0.21 | 4.87 | 0.67 | 0.52 | 0.92 | 0.70 |
| SD | 2.871 | 3.940 | 0.709 | 0.713 | 1.761 | 1.430 | 0.313 | 0.283 | 0.350 | 0.052 | 1.209 | 0.141 | 0.122 | 0.204 | 0.166 |
| CV (%) | 115.4 | 71.1 | 44.8 | 48.9 | 44.2 | 94.3 | 40.1 | 41.6 | 45.6 | 40.0 | 69.3 | 44.8 | 54.2 | 48.4 | 45.2 |
| N | 12 | 10 | 12 | 12 | 12 | 11 | 12 | 12 | 11 | 11 | 12 | 12 | 11 | 11 | 12 |

Note:

Data in bold = > 15 % CV (ALPHA samplers), or < 75 % capture in first of 2 denuders (DELTA)

Data underlined =  > 1 months exposure,  1  Silicone tube kinked, obstructing flow through denuders,

2  Pump not working properly or leak in system,  3  Contamination,

4   Water in system, denuders washed clean,  5  Suspected leak in system, between denuder and gas meter (although flow OK > 0.2 l min-1),  6   Problems with equipment,  7  Outliers,  ND 8 = No Data: Power off or equipment not working, ND 9 = No data: Sample lost,  ND 10 = No Data: Missing sample (stolen) or vandalised,  ND 11 = No Data: Non-return. KEY: D = DELTA, T = Passive (ALPHA)

Gaseous NH3 (ug NH3 m-3)

| Site | S23 | S24 | S25 | S25 | S26 | S27 | S28 | S29 | S30 | S31 | S32 | S33 | S33 | S34 | S35 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Method | D | D | D | T | D | D | D | T | D | D | T | D | T | D | D |
| Jan | 0.82 | 0.64 | 0.22 | 0.21 | 0.71 | 0.48 | 0.95 | 3.46 | 0.05 | 0.43 | 0.45 | 1.85 | 1.84 | 0.20 | 0.31 |
| Feb | 1.73 | ND 8 | 0.25 | 0.22 | 0.72 | 0.52 | 0.80 | 4.42 | 0.06 | 0.18 | 0.47 | 2.02 | 1.89 | 0.35 | 0.29 |
| Mar | 2.87 | 1.78 | 0.28 | 0.27 | 1.39 | 1.53 | 2.03 | 5.19 | 0.08 | 0.41 | 0.69 | 3.88 | 3.76 | 0.50 | 0.79 |
| Apr | 4.47 | 4.28 | 0.69 | 0.75 | 4.06 | 2.77 | 6.24 | 4.47 | 0.28 | 0.62 | 1.68 | 6.62 | 6.47 | 1.93 | 2.44 |
| May | 2.52 | 1.28 | 0.38 | 0.34 | 1.70 | 1.50 | 2.53 | 2.75 | 0.12 | 0.37 | 0.63 | 2.63 | 2.72 | 0.92 | 0.53 |
| Jun | 2.28 | 0.74 | 0.29 | 0.26 | 1.18 | 3.56 | 0.98 | 3.96 | 0.12 | 0.34 | 0.37 | 2.30 | 2.21 | 0.40 | 0.39 |
| Jul | 1.55 | 0.92 | 0.54 | ND 3 | 1.13 | ND 8 | 0.84 | 16.73 | 0.08 | 0.26 | 0.55 | 2.14 | 1.95 | 0.24 | 0.34 |
| Aug | 1.55 | 1.24 | 2.52 7 | 0.56 | 1.36 | ND 8 | 1.66 | 16.31 | 0.11 | 0.30 | 0.76 | 2.57 | 2.48 | 0.56 | 0.45 |
| Sep | 3.18 | 1.76 | ND 8 | 0.48 | 1.30 | ND 8 | 1.90 | 5.33 | 0.06 | 0.34 | 0.68 | 2.80 | 2.78 | 0.71 | 0.68 |
| Oct | 2.13 | 0.65 | 0.68 | 0.42 | 0.77 | 0.64 | 0.96 | 2.88 | 0.08 | 0.28 | 0.52 | 2.14 | 2.25 | 0.36 | 0.38 |
| Nov | 1.10 | 0.78 | 0.56 | 0.31 | 0.70 | ND 8 | 1.23 | 1.86 | 0.05 | 0.76 | 0.53 | 2.01 | 1.73 | 0.33 | 0.34 |
| Dec | 0.64 | 0.45 | 0.51 | 0.09 | 0.52 | 1.21 | 0.66 | 3.04 | 0.06 | 0.19 | 0.27 | 1.48 | 1.32 | 0.20 | 0.25 |
| Mean | 2.07 | 1.32 | 0.44 | 0.36 | 1.29 | 1.53 | 1.73 | 5.87 | 0.10 | 0.37 | 0.63 | 2.70 | 2.62 | 0.56 | 0.60 |
| Min | 0.64 | 0.45 | 0.22 | 0.09 | 0.52 | 0.48 | 0.66 | 1.86 | 0.05 | 0.18 | 0.27 | 1.48 | 1.32 | 0.20 | 0.25 |
| Max | 4.47 | 4.28 | 0.69 | 0.75 | 4.06 | 3.56 | 6.24 | 16.73 | 0.28 | 0.76 | 1.68 | 6.62 | 6.47 | 1.93 | 2.44 |
| SD | 1.089 | 1.080 | 0.178 | 0.186 | 0.943 | 1.114 | 1.535 | 5.083 | 0.064 | 0.169 | 0.358 | 1.372 | 1.367 | 0.483 | 0.602 |
| CV (%) | 52.6 | 81.9 | 40.4 | 52.3 | 72.9 | 72.9 | 88.7 | 86.6 | 66.7 | 45.2 | 56.5 | 50.7 | 52.2 | 86.3 | 100.7 |
| N | 12 | 11 | 10 | 11 | 12 | 8 | 12 | 12 | 12 | 12 | 12 | 12 | 12 | 12 | 12 |

| Site | S36C | S38 | S38B | S39 | S39B | S40 | S41 | S41 | S42 | S43 | S44 | S45 | S46 | S46 | S47 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Method | D | D | T | D | T | D | D | T | D | D | D | D | D | T | D |
| Jan | 3.95 | 0.12 | 1.11 | 0.62 | 0.56 | 6.75 | 0.10 | 0.08 | 3.33 | 1.41 | 1.93 | 0.19 | 0.91 | 1.24 | 0.10 |
| Feb | 4.22 | 0.47 | 1.54 | 1.19 | 1.26 | 3.02 | 0.34 | 0.13 | 3.28 | 1.17 | 3.08 | 2.04 | 0.99 | 1.37 | 0.82 |
| Mar | 4.42 | 0.66 | 1.63 | 2.95 | 2.84 | 9.48 | 0.27 | 0.15 | 5.08 | 2.80 | 3.87 | 0.43 | 1.94 | 3.26 | 0.20 |
| Apr | 7.48 | 1.50 | 2.63 | 3.91 | 4.77 | 7.24 | 0.41 | 0.32 | 7.68 | 5.38 | 7.29 | 1.04 | 4.34 | 5.63 | 0.31 |
| May | 4.27 | 0.77 | 1.54 | 1.52 | 1.51 | 2.59 | 0.26 | 0.24 | 3.70 | 2.04 | 7.98 | 0.54 | 2.32 | 2.29 | 0.25 |
| Jun | 3.65 | 0.45 | 1.01 | 1.31 | 1.36 | 1.93 | 0.44 | 0.42 | 2.53 | 1.72 | 5.79 | 1.31 | 1.07 | 0.97 | 0.43 |
| Jul | 3.33 | 0.38 | 1.06 | 1.35 | 1.37 | 2.99 | 0.85 | 0.82 | 3.50 | 1.43 | 1.91 | 0.24 | 0.95 | 1.84 | 0.36 |
| Aug | 3.67 | 0.60 | 1.64 | 1.46 | 1.61 | 3.64 | 1.30 | 1.26 | 5.47 | 2.29 | 2.43 | 0.29 | 1.32 | 2.30 | 0.21 |
| Sep | 4.02 | 1.03 | 1.90 | 1.62 | 1.57 | 4.23 | 2.02 | 1.88 | 6.14 | 1.74 | 5.12 | 0.49 | 1.73 | 2.71 | 0.35 |
| Oct | 3.33 | 0.97 | 1.77 | 0.86 | 0.96 | 4.18 | 0.61 | 0.57 | 4.16 | 1.68 | 3.87 | 0.68 | 0.60 | 1.38 | 0.35 |
| Nov | 3.33 | 0.78 | 1.30 | 2.32 | 2.28 | 2.45 | 0.20 | 0.19 | 4.29 | 1.05 | 1.95 | 0.32 | 0.55 | 1.87 | 0.11 |
| Dec | 2.50 | 0.36 | 1.10 | 0.81 | 1.02 | 1.33 | 0.18 | 0.11 | 2.87 | 0.64 | 1.74 | 0.83 | 0.46 | 0.83 | ND 8 |
| Mean | 4.01 | 0.67 | 1.52 | 1.66 | 1.76 | 4.15 | 0.58 | 0.51 | 4.34 | 1.95 | 3.91 | 0.70 | 1.43 | 2.14 | 0.32 |
| Min | 2.50 | 0.12 | 1.01 | 0.62 | 0.56 | 1.33 | 0.10 | 0.08 | 2.53 | 0.64 | 1.74 | 0.19 | 0.46 | 0.83 | 0.10 |
| Max | 7.48 | 1.50 | 2.63 | 3.91 | 4.77 | 9.48 | 2.02 | 1.88 | 7.68 | 5.38 | 7.98 | 2.04 | 4.34 | 5.63 | 0.82 |
| SD | 1.215 | 0.370 | 0.459 | 0.960 | 1.120 | 2.447 | 0.565 | 0.553 | 1.507 | 1.225 | 2.181 | 0.540 | 1.081 | 1.316 | 0.197 |
| CV (%) | 30.3 | 54.9 | 30.2 | 57.8 | 63.7 | 58.9 | 97.1 | 107.5 | 34.7 | 63.0 | 55.7 | 77.3 | 75.5 | 61.5 | 62.0 |
| N | 12 | 12 | 12 | 12 | 12 | 12 | 12 | 12 | 12 | 12 | 12 | 12 | 12 | 12 | 11 |

Note:

Data in bold = > 15 % CV (ALPHA samplers), or < 75 % capture in first of two denuders (DELTA)

Data underlined =  > 1 months exposure,  1  Silicone tube kinked, obstructing flow through denuders,

2  Pump not working properly or leak in system,  3  Contamination,

4   Water in system, denuders washed clean,  5  Suspected leak in system, between denuder and gas meter (although flow OK > 0.2 l min-1),  6   Problems with equipment,  7  Outliers,  ND 8 = No Data: Power off or equipment not working, ND 9 = No data: Sample lost,  ND 10 = No Data: Missing sample (stolen) or vandalised,  ND 11 = No Data: Non-return.

KEY: D = DELTA, T = Passive (ALPHA)

Gaseous NH3 (ug NH3 m-3)

| Site | S48 | S52A | S52B | S52C | S53 | S54 | S55 | S56 | S57B | S58 | S59 | S60C | S63 | S64 | S65 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Method | T | T | T | T | T | T | T | T | T | T | T | D | D | T | T |
| Jan | 0.90 | 1.63 | 1.53 | 2.34 | 2.35 | 2.21 | 0.24 | 1.00 | 1.17 | 1.67 | 0.63 | 1.20 | 0.29 | 0.04 | 0.06 |
| Feb | 4.16 | 2.46 | 2.06 | 2.60 | 2.88 | 2.83 | 0.29 | 1.00 | 2.61 | 1.47 | 0.47 | 1.48 | 1.72 | 0.19 | 0.04 |
| Mar | 2.86 | 3.21 | 2.58 | 5.57 | 9.63 | 7.64 | 1.39 | 2.73 | 2.61 | 13.82 | 1.44 | 1.18 | ND 8 | 0.87 | 0.35 |
| Apr | 4.15 | 5.30 | 4.45 | 8.30 | 4.80 | 4.28 | 1.39 | 0.68 | 3.32 | 5.32 | 1.68 | 1.83 | ND 8 | 1.95 | 0.23 |
| May | 1.82 | 2.06 | 1.59 | 3.16 | 1.60 | 2.40 | ND 11 | 1.42 | 2.84 | 1.76 | 0.39 | 1.18 | 1.10 | 0.36 | 0.10 |
| Jun | 1.62 | 2.50 | 2.51 | 4.64 | 1.15 | 2.04 | 0.25 | 1.04 | 0.95 | 1.19 | 0.42 | 0.90 | 0.85 | 0.21 | 0.07 |
| Jul | 0.99 | 1.01 | 1.35 | 1.17 | 0.73 | 1.41 | 0.25 | ND 10 | 1.45 | 2.18 | 0.91 | 1.18 | ND 8 | 0.16 | 0.05 |
| Aug | 1.50 | 1.48 | 1.54 | 1.85 | 1.82 | 2.07 | 0.65 | 1.47 | 1.26 | 2.68 | 0.91 | 1.53 | ND 8 | 0.27 | 0.04 |
| Sep | 1.92 | 1.41 | 1.41 | 1.59 | 2.00 | 2.68 | 1.38 | 0.98 | 1.58 | 2.64 | ND 11 | 1.66 | 0.72 | 0.26 | 0.06 |
| Oct | 2.44 | 3.64 | 2.16 | 7.51 | 1.34 | 1.68 | ND 11 | 1.15 | 1.71 | 3.06 | 1.48 | 1.59 | 0.61 | 0.11 | 1.12 |
| Nov | 1.32 | 1.54 | 1.18 | 1.58 | 2.46 | 2.02 | ND 11 | 0.61 | 1.27 | 1.28 | 0.84 | 1.43 | 0.59 | 0.24 | 0.04 |
| Dec | 1.00 | 1.43 | 0.96 | 1.14 | 1.39 | 1.94 | 0.22 | 0.45 | 0.47 | 1.15 | 0.34 | 0.80 | 0.38 | -0.01 | 0.02 |
| Mean | 2.06 | 2.31 | 1.94 | 3.46 | 2.68 | 2.77 | 0.67 | 1.14 | 1.77 | 3.19 | 0.86 | 1.33 | 0.78 | 0.39 | 0.18 |
| Min | 0.90 | 1.01 | 0.96 | 1.14 | 0.73 | 1.41 | 0.22 | 0.45 | 0.47 | 1.15 | 0.34 | 0.80 | 0.29 | -0.01 | 0.02 |
| Max | 4.16 | 5.30 | 4.45 | 8.30 | 9.63 | 7.64 | 1.39 | 2.73 | 3.32 | 13.82 | 1.68 | 1.83 | 1.72 | 1.95 | 1.12 |
| SD | 1.141 | 1.229 | 0.940 | 2.485 | 2.431 | 1.698 | 0.552 | 0.613 | 0.871 | 3.546 | 0.477 | 0.309 | 0.455 | 0.541 | 0.310 |
| CV (%) | 55.5 | 53.3 | 48.4 | 71.9 | 90.7 | 61.4 | 81.8 | 53.9 | 49.2 | 111.3 | 55.3 | 23.2 | 58.1 | 139.6 | 171.4 |
| N | 12 | 12 | 12 | 12 | 12 | 12 | 9 | 11 | 12 | 12 | 11 | 12 | 8 | 12 | 12 |

| Site | S66 | S67 | S68 | S70 | S71 | S72 | S74 | S75 | S76 | S76B | S77 | S78 | S78B | S79 | S80 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Method | T | T | T | D | D | T | D | T | D | T | D | D | T | D | D |
| Jan | 1.12 | 3.50 | 3.47 | 0.73 | 5.18 | 0.16 | ND 8 | 1.34 | 2.05 | 1.25 | 0.36 | 1.86 | 1.44 | 2.11 | 0.25 |
| Feb | 1.54 | 3.39 | 2.76 | 1.35 | 4.62 | 0.18 | 5.90 | 1.06 | 4.47 | 2.57 | 0.45 | 6.75 | 6.85 | 3.44 | 0.39 |
| Mar | 3.94 | 12.33 | 21.57 | 1.33 | 14.22 | 1.00 | 3.68 | 1.43 | 4.47 | 2.57 | 0.68 | 7.24 | 10.13 | ND 8 | 0.61 |
| Apr | 8.52 | 14.46 | 17.83 | 4.78 | 5.90 | 0.50 | 6.00 | 2.39 | 14.14 | 9.61 | 1.48 | 14.30 | 5.52 | 5.85 | 4.30 |
| May | 3.02 | 6.60 | 6.22 | 2.39 | 3.28 | 0.26 | 3.45 | 1.15 | 8.44 | 1.98 | 1.65 | 14.30 | 5.52 | 2.03 | 0.87 |
| Jun | 1.48 | 2.35 | 4.47 | 4.21 | 2.89 | 0.27 | 3.02 | 0.89 | 7.95 | 1.35 | 2.30 | 15.85 | 5.69 | 2.37 | 1.03 |
| Jul | 1.89 | 4.49 | 5.87 | 0.40 | 3.41 | 0.16 | 3.00 | 0.96 | 8.27 | 2.11 | 1.63 | 8.47 | 4.07 | 2.37 | 0.69 |
| Aug | 6.72 | 6.06 | 5.67 | 1.80 | 2.68 | 0.05 | 3.48 | 1.23 | 8.71 | 3.48 | 1.81 | 7.10 | 2.53 | 2.31 | 0.84 |
| Sep | 5.95 | 9.29 | 9.64 | 2.25 | 2.94 | 0.17 | 2.21 | 0.23 | 6.97 | 2.39 | 0.76 | 11.52 | 3.94 | 2.99 | 0.56 |
| Oct | 2.04 | 5.03 | 8.46 | 2.30 | 4.65 | 0.13 | 3.05 | 3.40 | 11.90 | 1.83 | 1.27 | 7.50 | 4.09 | 3.89 | 0.46 |
| Nov | 1.81 | 4.44 | 4.55 | 1.48 | 3.67 | 0.32 | 2.44 | 1.13 | 4.47 | 1.53 | 0.72 | 3.60 | 2.88 | 2.01 | 0.37 |
| Dec | 0.81 | 3.31 | 3.71 | 2.21 | 3.71 | 0.08 | 3.84 |  | 2.48 | 0.62 | 0.45 | 12.89 | 9.97 | 2.55 | 0.18 |
| Mean | 3.24 | 6.27 | 7.85 | 2.10 | 4.76 | 0.27 | 3.64 | 1.38 | 7.03 | 2.61 | 1.13 | 9.28 | 5.22 | 2.90 | 0.88 |
| Min | 0.81 | 2.35 | 2.76 | 0.40 | 2.68 | 0.05 | 2.21 | 0.23 | 2.05 | 0.62 | 0.36 | 1.86 | 1.44 | 2.01 | 0.18 |
| Max | 8.52 | 14.46 | 21.57 | 4.78 | 14.22 | 1.00 | 6.00 | 3.40 | 14.14 | 9.61 | 2.30 | 15.85 | 10.13 | 5.85 | 4.30 |
| SD | 2.515 | 3.828 | 5.932 | 1.285 | 3.139 | 0.260 | 1.241 | 0.841 | 3.651 | 2.328 | 0.640 | 4.452 | 2.713 | 1.150 | 1.108 |
| CV (%) | 77.7 | 61.0 | 75.5 | 61.1 | 65.9 | 94.9 | 34.1 | 60.8 | 52.0 | 89.3 | 56.6 | 48.0 | 52.0 | 39.6 | 125.9 |
| N | 12 | 12 | 12 | 12 | 12 | 12 | 11 | 11 | 12 | 12 | 12 | 12 | 12 | 11 | 12 |

Note:

Data in bold = > 15 % CV (ALPHA samplers), or < 75 % capture in first of two denuders (DELTA)

Data underlined =  > 1 months exposure,  1  Silicone tube kinked, obstructing flow through denuders,

2  Pump not working properly or leak in system,  3  Contamination,

4   Water in system, denuders washed clean,  5  Suspected leak in system, between denuder and gas meter (although flow OK > 0.2 l min-1),  6   Problems with equipment,  7  Outliers,  ND 8 = No Data: Power off or equipment not working, ND 9 = No data: Sample lost,  ND 10 = No Data: Missing sample (stolen) or vandalised,  ND 11 = No Data: Non-return.

KEY: D = DELTA, T = Passive (ALPHA)

Gaseous NH3 (ug NH3 m-3)

| Site | S82 | S83 | S84 | S86 | S87 | S89 | S90 | S91 | S92 | S93 | S94 | S95 | S95 | S96 | S97 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Method | T | D | T | T | T | T | T | T | T | D | D | D | T | D | T |
| Jan | 3.69 | 0.97 | 0.20 | 2.61 | 1.16 | 0.01 | 0.32 | 0.03 | 0.03 | 0.15 | 0.28 | 0.22 | 0.11 | 1.00 | 0.77 |
| Feb | 7.01 | 1.07 | 0.43 | 0.91 | 1.37 | 0.01 | 0.14 | 0.03 | 0.05 | 0.09 | 0.27 | 0.20 | 0.17 | 0.87 | 3.94 |
| Mar | 12.08 | 0.60 | 0.75 | 1.03 | 2.78 | 0.04 | 0.34 | 0.05 | 0.07 | 0.48 | 0.77 | 0.25 | 0.19 | 1.24 | 2.58 |
| Apr | 6.53 | 3.34 | 2.62 | 1.46 | 3.30 | 0.15 | stopped | 0.18 | stopped | 0.48 | 2.02 | 0.72 | 0.65 | 1.86 | 8.05 |
| May | 3.32 | 1.23 | 0.79 | 0.78 | 3.38 | 0.08 |  | 0.10 |  | 0.22 | 1.40 | 0.65 | 0.44 | 0.82 | 8.54 |
| Jun | 2.15 | 1.25 | 0.52 | 0.67 | 1.30 | 0.01 |  | 0.05 |  | 0.10 | 0.40 | 1.19 | 0.53 | 0.75 | 0.89 |
| Jul | 2.59 | 0.89 | 0.38 | 0.35 | 1.18 | 0.03 |  | 0.03 |  | 0.09 | 0.40 | 0.74 | 0.76 | 0.99 | 0.96 |
| Aug | 4.49 | 0.49 | 0.63 | 0.65 | 1.60 | 0.01 |  | 0.02 |  | 0.12 | 0.56 | 0.64 | 0.47 | 1.23 | 1.42 |
| Sep | 6.49 | 1.31 | 0.76 | 0.58 | 1.65 | 0.02 |  | 0.03 |  | 0.12 | 0.90 | 0.45 | 0.30 | 1.71 | 2.53 |
| Oct | 9.26 | 3.78 | 0.41 | 0.46 | 1.23 | 0.03 |  | 0.05 |  | ND 3 | 0.29 | 0.59 | 0.25 | 1.10 | 0.79 |
| Nov | 6.61 | 1.17 | 0.42 | 0.75 | 0.99 | 0.00 |  | 0.01 |  | 0.06 | 0.36 | 0.29 | 0.24 | 0.97 | 1.01 |
| Dec | 2.95 | 0.86 | 0.21 | 0.33 | 1.05 | 0.02 |  | 0.02 |  | 0.09 | 0.23 | *0.00 5 | 0.07 | 0.69 | 0.57 |
| Mean | 5.60 | 1.41 | 0.68 | 0.88 | 1.75 | 0.04 | 0.27 | 0.05 | 0.05 | 0.18 | 0.66 | 0.54 | 0.35 | 1.10 | 2.67 |
| Min | 2.15 | 0.49 | 0.20 | 0.33 | 0.99 | 0.00 | 0.14 | 0.01 | 0.03 | 0.06 | 0.23 | 0.20 | 0.07 | 0.69 | 0.57 |
| Max | 12.08 | 3.78 | 2.62 | 2.61 | 3.38 | 0.15 | 0.34 | 0.18 | 0.07 | 0.48 | 2.02 | 1.19 | 0.76 | 1.86 | 8.54 |
| SD | 2.986 | 1.038 | 0.643 | 0.627 | 0.879 | 0.042 | 0.109 | 0.048 | 0.024 | 0.153 | 0.550 | 0.298 | 0.220 | 0.363 | 2.813 |
| CV (%) | 53.3 | 73.4 | 95.0 | 71.1 | 50.3 | 115.6 | 40.6 | 96.8 | 47.4 | 85.2 | 83.7 | 55.2 | 63.3 | 32.9 | 105.3 |
| N | 12 | 12 | 12 | 12 | 12 | 12 | 3 | 12 | 3 | 11 | 12 | 11 | 12 | 12 | 12 |

| Site | S98 | S99 | S100 | S102 | S103 | S104 |  |  |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Method | T | D | D | T | D | T |  |  |  |  |  |  |  |  |  |
| Jan | 1.04 | 0.46 | 0.16 | 1.64 | 0.48 | 4.05 |  |  |  |  |  |  |  |  |  |
| Feb | 1.21 | 0.70 | 0.50 | 2.09 | 0.48 | 5.88 |  |  |  |  |  |  |  |  |  |
| Mar | 2.71 | 0.97 | 0.35 | 10.34 | 0.89 | 5.01 |  |  |  |  |  |  |  |  |  |
| Apr | 4.83 | 1.52 | 1.34 | ND 8 | 1.40 | 9.99 |  |  |  |  |  |  |  |  |  |
| May | 1.94 | 0.88 | 0.49 | 2.84 | 0.46 | 7.28 |  |  |  |  |  |  |  |  |  |
| Jun | 1.41 | 0.77 | 0.55 | 2.00 | 0.37 | 15.01 |  |  |  |  |  |  |  |  |  |
| Jul | 1.32 | 0.75 | 0.24 | 0.95 | 0.39 | 12.00 |  |  |  |  |  |  |  |  |  |
| Aug | 1.81 | 0.88 | 0.34 | 2.88 | 0.61 | 7.74 |  |  |  |  |  |  |  |  |  |
| Sep | 2.05 | 0.85 | 0.40 | 2.85 | 0.70 | 11.16 |  |  |  |  |  |  |  |  |  |
| Oct | 0.49 | 0.60 | 0.32 | 4.19 | 0.92 | 7.92 |  |  |  |  |  |  |  |  |  |
| Nov | 1.92 | 0.35 | 0.25 | 2.28 | 0.60 | 7.96 |  |  |  |  |  |  |  |  |  |
| Dec | 0.97 | 0.35 | 0.14 | 0.90 | 0.20 | 5.61 |  |  |  |  |  |  |  |  |  |
| Mean | 1.81 | 0.76 | 0.42 | 3.00 | 0.63 | 8.30 |  |  |  |  |  |  |  |  |  |
| Min | 0.49 | 0.35 | 0.14 | 0.90 | 0.20 | 4.05 |  |  |  |  |  |  |  |  |  |
| Max | 4.83 | 1.52 | 1.34 | 10.34 | 1.40 | 15.01 |  |  |  |  |  |  |  |  |  |
| SD | 1.122 | 0.319 | 0.318 | 2.610 | 0.321 | 3.210 |  |  |  |  |  |  |  |  |  |
| CV (%) | 62.0 | 42.1 | 75.1 | 87.1 | 51.4 | 38.7 |  |  |  |  |  |  |  |  |  |
| N | 12 | 12 | 12 | 11 | 12 | 12 |  |  |  |  |  |  |  |  |  |

Note:

Data in bold = > 15 % CV (ALPHA samplers), or < 75 % capture in first of two denuders (DELTA)

Data underlined =  > 1 months exposure,  1  Silicone tube kinked, obstructing flow through denuders,

2  Pump not working properly or leak in system,  3  Contamination,

4   Water in system, denuders washed clean,  5  Suspected leak in system, between denuder and gas meter (although flow OK > 0.2 l min-1),  6   Problems with equipment,  7  Outliers,  ND 8 = No Data: Power off or equipment not working, ND 9 = No data: Sample lost,  ND 10 = No Data: Missing sample (stolen) or vandalised,  ND 11 = No Data: Non-return

KEY: D = DELTA, T = Passive (ALPHA)

## Monthly particulate ammonium data in the UK NAMN

Particulate NH4+ (µg NH4+ m-3)

| Site | S1L | S 1R | S3B | S6B | S8B | S11 | S12 | S16 | S17 | S18L | S18R | S19 | S21 | S22 | S23 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Jan | 0.13 | 0.13 | 0.01 | 0.29 | 0.33 | 0.77 | 0.03 | 0.30 | 1.87 | 0.11 | 0.11 | 0.03 | 0.08 | 0.26 | 0.21 |
| Feb | 0.39 | 0.46 | 0.15 | 1.01 | 0.48 | 0.74 | 0.16 | 1.58 | 1.51 | 0.37 | 0.47 | 0.10 | 0.25 | 0.30 | 0.60 |
| Mar | 1.12 | 1.13 | 0.39 | 2.39 | 1.22 | 1.36 | 0.11 | 2.08 | 2.52 | 0.80 | 0.61 | 0.62 | 0.68 | 0.79 | 1.04 |
| Apr | 0.71 | 0.96 | 0.44 | 2.06 | 2.78 | 0.29 | 0.49 | 1.12 | 2.91 | 1.25 | 1.08 | 0.37 | 0.95 | 1.38 | 2.39 |
| May | 0.43 | 0.38 | 0.17 | 0.84 | ND 9 | 0.40 | 0.24 | 0.77 | 0.62 | 0.41 | 0.40 | 0.18 | 0.37 | 0.37 | 0.58 |
| Jun | 1.07 | 1.02 | 0.23 | 1.83 | 0.98 | 0.77 | 0.36 | 2.30 | 1.12 | 1.08 | 0.88 | 0.26 | 0.64 | 0.88 | 0.78 |
| Jul | 0.31 | 0.31 | 0.09 | 0.41 | 0.98 | 0.41 | 0.17 | 0.45 | 0.34 | 0.27 | 0.21 | 0.18 | 0.18 | 0.46 | 0.24 |
| Aug | 0.18 | 0.18 | 0.07 | 0.29 | 5.99 | 0.25 | 0.14 | 0.41 | 0.35 | 0.18 | 0.20 | 0.11 | 0.16 | 0.14 | 0.35 |
| Sep | 0.20 | 0.23 | 0.07 | 0.16 | 0.59 | 1.03 | 0.06 | 0.35 | 0.32 | 0.19 | 0.16 | -0.01 7 | 0.12 | ND 8 | 0.48 |
| Oct | 0.94 | 0.89 | 0.27 | 1.81 | 1.58 | 1.03 | 0.25 | 1.67 | ND 8 | 0.83 | 0.75 | 0.57 | 0.80 | 0.88 | 1.16 |
| Nov | 0.36 | 0.36 | 0.05 | 0.79 | 0.49 | 0.74 | -0.04 7 | 0.78 | 0.80 | 0.42 | 0.31 | 0.33 | 0.22 | 0.38 | 0.40 |
| Dec | 0.98 | 0.88 | 0.12 | 1.30 | 1.22 | 3.63 | 0.21 | 1.68 | 1.61 | 0.59 | 0.53 | 0.40 | 0.43 | 0.47 | 0.78 |
| Mean | 0.57 | 0.58 | 0.17 | 1.10 | 1.51 | 0.95 | 0.20 | 1.12 | 1.27 | 0.54 | 0.48 | 0.29 | 0.41 | 0.57 | 0.75 |
| Min | 0.13 | 0.13 | 0.01 | 0.16 | 0.33 | 0.25 | 0.03 | 0.30 | 0.32 | 0.11 | 0.11 | 0.03 | 0.08 | 0.14 | 0.21 |
| Max | 1.12 | 1.13 | 0.44 | 2.39 | 5.99 | 3.63 | 0.49 | 2.30 | 2.91 | 1.25 | 1.08 | 0.62 | 0.95 | 1.38 | 2.39 |
| SD | 0.37 | 0.37 | 0.14 | 0.77 | 1.64 | 0.91 | 0.13 | 0.71 | 0.90 | 0.37 | 0.31 | 0.19 | 0.29 | 0.37 | 0.60 |
| CV (%) | 65.5 | 63.6 | 80.2 | 70.1 | 108.0 | 95.3 | 65.4 | 63.5 | 70.6 | 68.5 | 64.7 | 66.7 | 71.7 | 64.3 | 79.3 |
| N | 12 | 12 | 12 | 12 | 11 | 12 | 11 | 12 | 11 | 12 | 12 | 11 | 12 | 11 | 12 |

| Site | S24 | S25 | S30 | S31 | S32 | S33 | S34 | S35 | S36C | S38 | S39 | S40 | S41 | S42 | S44 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Jan | 0.53 | 0.10 | 0.03 | 0.37 | 0.33 | 0.40 | 0.28 | 0.63 | 0.69 | 1.20 | 0.84 | 0.83 | 0.07 | 0.69 | 0.22 |
| Feb | ND 8 | 0.41 | 0.10 | 0.18 | 0.88 | 1.10 | 0.67 | 0.64 | 1.78 | 1.14 | 1.24 | 1.08 | 1.06 | 0.59 | 0.53 |
| Mar | 2.75 | 0.17 | 0.15 | 1.08 | 1.47 | 2.91 | 1.05 | 1.92 | 2.55 | 2.99 | 2.13 | 2.60 | 0.65 | 1.75 | 2.05 |
| Apr | 2.53 | 0.68 | 0.62 | 0.85 | 1.50 | 1.64 | 3.58 | 2.28 | 1.62 | 1.25 | 3.04 | 2.44 | 0.40 | 0.35 | 0.59 |
| May | 0.85 | 0.25 | 0.18 | 0.35 | 0.70 | 1.00 | 0.89 | 0.52 | 1.20 | 1.27 | 0.65 | 0.84 | 0.24 | 1.23 | 0.47 |
| Jun | 1.35 | 0.45 | ND 9 | 0.60 | 0.78 | 1.45 | 0.92 | 0.68 | 1.54 | 0.41 | 1.10 | 1.34 | 0.33 | 0.54 | 0.99 |
| Jul | 0.63 | 0.73 | 0.07 | 0.25 | 0.44 | 0.81 | 0.25 | 0.46 | 0.91 | 0.36 | 0.48 | 0.70 | 0.15 | 0.47 | 0.46 |
| Aug | 0.69 | ND 8 | 0.08 | 0.15 | 0.30 | 0.52 | 0.34 | 0.42 | 0.95 | 0.35 | 0.68 | 0.58 | 0.07 | 0.55 | 0.23 |
| Sep | 0.85 | ND 8 | 0.05 | 0.23 | 0.46 | 0.85 | 0.52 | 0.76 | 1.15 | 1.01 | 0.68 | 0.76 | 0.16 | 0.71 | 0.42 |
| Oct | 2.28 | ND 8 | 0.25 | 1.00 | 1.41 | 2.05 | 1.27 | 1.20 | 3.04 | 0.88 | 1.82 | 1.67 | 0.31 | 1.56 | 1.12 |
| Nov | 1.07 | 0.29 | 0.10 | 0.68 | 0.70 | 1.34 | 0.44 | 0.43 | 1.16 | 0.51 | 0.93 | 1.30 | 0.08 | 0.72 | 0.46 |
| Dec | 1.72 | 0.10 | 0.12 | 0.79 | 1.07 | 1.60 | 0.95 | 1.05 | 1.95 | 1.18 | 1.59 | 1.64 | 0.22 | 1.27 | 0.43 |
| Mean | 1.39 | 0.35 | 0.16 | 0.54 | 0.83 | 1.31 | 0.93 | 0.92 | 1.54 | 1.05 | 1.27 | 1.31 | 0.31 | 0.87 | 0.66 |
| Min | 0.53 | 0.10 | 0.03 | 0.15 | 0.30 | 0.40 | 0.25 | 0.42 | 0.69 | 0.35 | 0.48 | 0.58 | 0.07 | 0.35 | 0.22 |
| Max | 2.75 | 0.73 | 0.62 | 1.08 | 1.50 | 2.91 | 3.58 | 2.28 | 3.04 | 2.99 | 3.04 | 2.60 | 1.06 | 1.75 | 2.05 |
| SD | 0.81 | 0.24 | 0.16 | 0.33 | 0.44 | 0.70 | 0.90 | 0.61 | 0.70 | 0.71 | 0.76 | 0.67 | 0.29 | 0.46 | 0.51 |
| CV (%) | 58.4 | 66.6 | 103.2 | 61.2 | 52.4 | 53.6 | 96.6 | 66.1 | 45.2 | 68.3 | 60.1 | 50.7 | 92.3 | 53.1 | 77.0 |
| N | 11 | 9 | 11 | 12 | 12 | 12 | 12 | 12 | 12 | 12 | 12 | 12 | 12 | 12 | 12 |

Note:

Data in bold = > 15 % CV (ALPHA samplers), or < 75 % capture in first of two denuders (DELTA)

Data underlined =  > 1 months exposure,  1  Silicone tube kinked, obstructing flow through denuders,

2  Pump not working properly or leak in system,  3  Contamination,

4   Water in system, denuders washed clean,  5  Suspected leak in system, between denuder and gas meter (although flow OK > 0.2 l min-1),  6   Problems with equipment,  7  Outliers,  ND 8 = No Data: Power off or equipment not working, ND 9 = No data: Sample lost,  ND 10 = No Data: Missing sample (stolen) or vandalised,  ND 11 = No Data: Non-return

Particulate NH4+ (µg NH4+ m-3)

| Site | S45 | S47 | S60C | S70 | S74 | S76 | S77 | S78 | S79 | S80 | S83 | S95B | S97 | S98 | S99 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Jan | 0.13 | 0.09 | 0.25 | 0.29 | ND 8 | 0.83 | 0.54 | 0.09 | 0.27 | 0.09 | 0.59 | 0.14 | 0.95 | 0.47 | 0.37 |
| Feb | 0.20 | 0.23 | 0.63 | 0.34 | 0.81 | 2.07 | 0.36 | 0.44 | 0.42 | 0.44 | 0.89 | 0.24 | 0.36 | 1.03 | 0.47 |
| Mar | 0.84 | 0.62 | 1.36 | 1.66 | 0.95 | 2.07 | nd | 0.93 | ND 8 | 0.93 | 1.46 | 0.28 | 2.10 | 2.20 | 1.02 |
| Apr | 1.06 | 0.43 | 1.00 | 1.49 | 1.11 | 3.75 | 1.09 | 0.81 | 0.46 | 0.76 | 3.30 | 0.95 | 1.36 | 2.82 | 2.46 |
| May | 0.25 | 0.18 | 0.44 | 0.76 | 0.61 | 0.07 | 0.28 | 0.81 | 0.30 | 0.31 | 1.08 | 0.25 | 0.73 | 0.82 | 0.74 |
| Jun | 0.53 | 0.24 | 1.13 | 0.94 | 0.64 | 2.35 | 0.51 | 0.76 | 0.41 | 0.56 | 1.30 | 0.63 | 1.10 | 1.11 | 1.33 |
| Jul | 0.22 | 0.17 | 0.39 | 0.30 | 0.27 | 0.30 | 0.15 | 0.64 | 0.41 | 0.18 | 0.65 | 0.14 | 0.76 | ND 8 | 0.45 |
| Aug | 0.08 | 0.08 | 0.28 | 0.24 | 0.22 | 0.74 | 0.10 | 0.21 | 0.16 | 0.19 | 0.72 | 0.11 | 0.73 | 0.58 | 0.42 |
| Sep | 0.21 | 0.36 | 0.30 | 0.52 | 0.14 | 0.42 | 0.11 | 0.23 | 0.35 | 0.20 | 1.51 | 0.08 | 1.01 | 0.80 | 0.87 |
| Oct | 0.83 | 0.29 | 1.25 | 1.03 | 0.63 | 0.58 | 0.57 | 0.92 | 0.85 | 0.68 | 1.92 | 0.58 | 2.14 | 1.90 | 1.32 |
| Nov | 0.27 | 0.11 | 0.30 | 0.42 | 0.26 | 0.80 | 0.19 | 0.33 | 0.27 | 0.26 | 1.14 | 0.09 | 1.18 | 0.69 | 0.53 |
| Dec | 0.74 | ND 8 | 1.15 | 0.79 | 1.23 | 1.67 | 0.27 | 0.28 | 0.81 | 0.63 | ND 8 | -0.00 5 | 1.54 | 1.50 | 1.95 |
| Mean | 0.45 | 0.25 | 0.71 | 0.73 | 0.62 | 1.30 | 0.38 | 0.54 | 0.43 | 0.44 | 1.32 | 0.32 | 1.16 | 1.27 | 0.99 |
| Min | 0.08 | 0.08 | 0.25 | 0.24 | 0.14 | 0.07 | 0.10 | 0.09 | 0.16 | 0.09 | 0.59 | 0.08 | 0.36 | 0.47 | 0.37 |
| Max | 1.06 | 0.62 | 1.36 | 1.66 | 1.23 | 3.75 | 1.09 | 0.93 | 0.85 | 0.93 | 3.30 | 0.95 | 2.14 | 2.82 | 2.46 |
| SD | 0.34 | 0.17 | 0.43 | 0.48 | 0.37 | 1.09 | 0.29 | 0.31 | 0.22 | 0.27 | 0.77 | 0.28 | 0.55 | 0.75 | 0.67 |
| CV (%) | 75.3 | 64.9 | 61.5 | 65.3 | 60.1 | 83.5 | 76.7 | 57.1 | 50.9 | 62.3 | 58.2 | 88.4 | 46.9 | 59.6 | 66.9 |
| N | 12 | 11 | 12 | 12 | 11 | 12 | 11 | 12 | 11 | 12 | 11 | 11 | 12 | 11 | 12 |

| Site | S100 | S102 | S103 |  |  |  |  |  |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Method | 0.13 | 0.62 | 0.30 |  |  |  |  |  |  |  |  |  |  |  |  |
| Jan | 0.76 | 1.59 | 0.30 |  |  |  |  |  |  |  |  |  |  |  |  |
| Feb | 0.90 | 1.91 | 1.96 |  |  |  |  |  |  |  |  |  |  |  |  |
| Mar | 1.66 | ND 8 | 2.88 |  |  |  |  |  |  |  |  |  |  |  |  |
| Apr | 0.54 | 0.94 | 0.34 |  |  |  |  |  |  |  |  |  |  |  |  |
| May | 0.90 | 1.39 | 0.75 |  |  |  |  |  |  |  |  |  |  |  |  |
| Jun | 0.29 | 0.69 | 0.32 |  |  |  |  |  |  |  |  |  |  |  |  |
| Jul | 0.18 | 0.66 | 0.30 |  |  |  |  |  |  |  |  |  |  |  |  |
| Aug | 0.25 | 0.64 | 0.72 |  |  |  |  |  |  |  |  |  |  |  |  |
| Sep | 0.80 | 0.77 | 0.83 |  |  |  |  |  |  |  |  |  |  |  |  |
| Oct | 0.36 | 1.09 | 0.38 |  |  |  |  |  |  |  |  |  |  |  |  |
| Nov | 0.67 | 1.82 | 0.42 |  |  |  |  |  |  |  |  |  |  |  |  |
| Dec | 0.13 | 0.62 | 0.30 |  |  |  |  |  |  |  |  |  |  |  |  |
| Mean | 0.62 | 1.10 | 0.79 |  |  |  |  |  |  |  |  |  |  |  |  |
| Min | 0.13 | 0.62 | 0.30 |  |  |  |  |  |  |  |  |  |  |  |  |
| Max | 1.66 | 1.91 | 2.88 |  |  |  |  |  |  |  |  |  |  |  |  |
| SD | 0.43 | 0.49 | 0.81 |  |  |  |  |  |  |  |  |  |  |  |  |
| CV (%) | 69.7 | 44.9 | 102.4 |  |  |  |  |  |  |  |  |  |  |  |  |
| N | 12 | 11 | 12 |  |  |  |  |  |  |  |  |  |  |  |  |

Note:

Data in bold = > 15 % CV (ALPHA samplers), or < 75 % capture in first of two denuders (DELTA)

Data underlined =  > 1 months exposure,  1  Silicone tube kinked, obstructing flow through denuders,

2  Pump not working properly or leak in system,  3  Contamination,

4   Water in system, denuders washed clean,  5  Suspected leak in system, between denuder and gas meter (although flow OK > 0.2 l min-1),  6   Problems with equipment,  7  Outliers,  ND 8 = No Data: Power off or equipment not working, ND 9 = No data: Sample lost,  ND 10 = No Data: Missing sample (stolen) or vandalised,  ND 11 = No Data: Non-return

# Text boxes

NH3